## Slide 1: MB-GCC
The MicroBlaze GNU C Compiler

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the function of the MicroBlaze™ compiler on a given set of “C”, “C++” or Assembly files
Describe the MicroBlaze Application Binary Interface
Describe the optimization and debugging options of MB-GCC
List the different runtime routines and their appropriate functions
Specify the functionality and make-up of an object file
Describe the use of linker script
Describe the interrupt handling

## Slide 3: Introduction
What is a compiler?
A program that converts another program from some source language to machine language
Compiler
Source code
Object code
Notes: A compiler is a program that converts another program from some source language (or programming language) to machine language (object code). Some compilers output assembly language, which is then converted to machine language by a separate assembler.
A compiler is distinguished from an assembler by the fact that each input statement does not, in general, correspond to a single machine instruction or fixed sequence of instructions. A compiler may support such features as automatic allocation of variables, arbitrary arithmetic expressions, control structures such as FOR and WHILE loops, variable scope, input/output operations, higher-order functions, and portability of source code.

## Slide 4: Introduction
What are the Input Source files to mb-gcc?
C source file: file.c
C++ source file: file.c++, file.cpp, file.cxx, file.C, file.cc
Assembly file with pre-processor directives: file.S
Assembly file without pre-processor directives: file.s
What are the libraries used by mb-gcc ?
Libxil.a : contains drivers and initialisation files
libc.a : standard C libraries
libm.a : math libraries

## Slide 5: Outline
What is MB-GCC and How is It Made Up?
MicroBlaze Application Binary Interface
Optimization & Debugging Options
Runtime Routines & The Object File
Interrupt Handling
Summary

## Slide 6: What is MB-GCC?
MicroBlaze™ GNU cross compiler
The tool used to transform your C, C++, Assembly files into a MicroBlaze executable format
Freeware Open Source
Command line based
Notes: A compiler is called a cross-compiler when it runs on one platform (Windows or Solaris for MB-GCC) and produces code for another (MicroBlaze processor) as opposed to a native code compiler that produces code for the platform on which it runs.

## Slide 7: What is MB-GCC?
MicroBlaze GNU Cross Compiler is made up as follow:
mb-gcc.exe - The top-level GNU program
  Calls programs listed below as necessary
cpp0.exe - The preprocessor
  Replaces all macros with definitions from the sources and header files
cc1.exe - The C compiler
  Translates the user’s C into assembly
  Optimizes code (reduces instructions, fills the pipeline)
cc1plus.exe - The C++ compiler
  Translates the user’s C++ into assembly
  Optimizes code (reduces instructions, fills the pipeline)
Notes: Given a set of C source files, a MicroBlaze™ executable is created as follows:
1. To compile and link, run the following:
mb-gcc file1.c file2.c
The MicroBlaze compiler searches the MICROBLAZE Environment Variable for libraries and include files.
If the MICROBLAZE environment variable is not set, use the -L option to point to the directory containing the libc.a and libm.a libraries.
mb-gcc -L<dir1-name> -I<dir2-name> -B<dir3-name> file1.c file2.c MicroBlaze compiler will look into dir1-name for libraries and dir2 name for header files and dir3-name for C runtime libraries. A MicroBlaze executable file, a.out, is created. For including any of the math functions, include -lm in the command line for mb-gcc.
2. For further information on mb-gcc options, run one of the following:
- mb-gcc --help
- info gcc
The latter will give you the info page of Solaris gcc on which mb-gcc is based. You can also refer to the MicroBlaze GNU Compiler Tools documentation for more details on use of MicroBlaze GNU tools.

## Slide 8: What is MB-GCC?
mb-as.exe - The assembler
  Translates assembly language into machine language
mb-ld.exe - The linker loader
  Combines separately assembled files, libraries and initialisation code into a single binary executable .elf file
mb-size.exe - The size utility
  Gives information about the object file size
mb-objdump.exe - The object file utility
  Disassembles and displays information from the object file
Notes: The mb-size program included with the MDK will help to determine the size of your program. It operates on the compiled source code file.
> mb-size code/system.out
...text......data......bss......dec.....hex......filename
...1648.....80.......1028....2756...ac4.....code/system.out
The results of mb-size show the size of the different portions of the program.
- The "text" section shows the decimal number of bytes taken up by the constant program data.
- The "data" section shows the decimal number of bytes taken up by the initialized variable data.
- The "bss" or "block started by symbol" section shows the decimal number of bytes taken up by the variable data.
- The "dec" and "hex" section show the total number of bytes the program takes up in decimal and hexadecimal, respectively.

## Slide 9: MB-GCC Tool Flow
Input C or C++ Files
cc1
cc1plus
mb-as
mb-ld
Output *.elf File
Notes: When mb-gcc top level program is called, depending on which kind of input source files are presented, mb-gcc will call the appropriate ones:
- If the input source code is in C, then cc1.exe will be called.
- If the input source code is in C++, then cc1plus is called.

## Slide 10: Launching MB-GCC
mb-gcc –xl-mode-xx {–g} <input.c> -L<libs> -I<include> -o <output.out>
Adds debugging links to the object file
Input ‘C’ or ‘C++’ files
Location of any libraries
Location of the Include files
Output Object file
xl-mode-executable/xmdstub/bootstrap/bootstrap-reset/xilkernel - Different Initialization modes
Notes: The slide above shows a typical command line for the mb-gcc compiler.
-xl-mode-executable – In this mode, the code is compiled and linked so that execution starts at 0x0000_0000 Hex. This is the starting point for the program counter and so the executable would run as expected.
-xl-mode-xmdstub – In this mode, the MicroBlaze™ soft processor is expected to be running the Xilinx-supplied XMD debug stub. This takes up memory in the MicroBlaze system to run debugging routines. If executable code is to be put into MicroBlaze, along with the debugging stub, then they must not occupy the same memory addresses. This attribute offsets the executable to a higher place in memory.
-xl-mode-bootstrap – Generates code that can be downloaded using the bootstrap loader.
-g This switch is used for debugging. If the –g switch is specified, information about the C source code is embedded into the .elf file so the user can load the .out file into the debugger and have information about the C source code, cross-referenced with the assembly.
-L –I – These switches specify the locations of the Library and Include files for the project. These files and directories are generated by Libgen.
-o This specifies the output file name for the compiled object.

## Slide 11: Outline
What is MB-GCC and How is It Made Up?
MicroBlaze Application Binary Interface
Optimization & Debugging Options
Runtime Routines & The Object File
Interrupt Handling
Summary

## Slide 12: Assembly Data Types Convention
MicroBlaze data Types (For Assembly programs)
Corresponding ANSI C data Types
Size (bytes)
data8
char
1
data16
short
2
data32
data32
int
4
long int
4
data32
enum
4
data16/data32
pointer
2/4
Notes: The data types used by MicroBlaze™ assembly programs are shown in the slide above. Data types such as data8, data16, and data32 are used in place of the usual byte, halfword, and word.
Pointers to small data areas, which can be accessed by global pointers are data16. This optimisation takes place when the compiler is instructed to use it following the Switch -mxl-gp-opt.

## Slide 13: MicroBlaze Register Types
MicroBlaze™ architecture defines:
Register file of 32 general purpose registers: R0-R31
  Dedicated: {R0 to R2, R13 to R18}
  Volatile: {R3 to R12}
  Non-volatile: {R19 to R31}
Two special purpose registers: PC and MSR
  PC: Program Counter
  MSR: Machine Status Register
Notes: The architecture for the MicroBlaze soft processor defines 32 general purpose registers (GPRs). These registers are classified as volatile, non-volatile, and dedicated.
• The volatile registers are used as temporaries and do not retain values across the function calls. Registers R3 through R12 are volatile, of which R3 and R4 are used for returning values to the caller function, if any. Registers R5 through R10 are used for passing parameters between sub-routines.
• Registers R19 through R31 retain their contents across function calls and are hence termed as non-volatile registers. The callee function is expected to save those non-volatile registers, which are being used. These are typically saved to the stack during the prologue and then reloaded during the epilogue.
• MicroBlaze soft processor has certain special registers such as program counter (rpc) and machine status register (rmsr). These registers are not mapped directly to the register file and hence the usage of these registers is different from the general purpose registers. The value from rmsr and rpc can be transferred to general purpose registers by using mts and mfs instructions.

## Slide 14: Registers Usage Convention
Register
Type
Purpose
R0
Dedicated
Dedicated
R1
R2
R3-R4
R5-R10
R11-R12
R13
R14
R15
R16
R17
R18
R19-R31
RPC
RMSR
Dedicated
Volatile
Volatile
Dedicated
Dedicated
Dedicated
Dedicated
Dedicated
Non-Volatile
Special
Special
Volatile
Dedicated
Value 0
Stack Pointer
Read-only small data area anchor
Return values
Passing parameters/Temporaries
Temporaries
Read-write small data area anchor
Return address for Interrupt
Return address for Sub-routine
Return address for Trap (Debugger)
Return address for Exceptions
Reserved for Assembler
Must be saved across function calls
Program Counter
Machine Status Register
Notes: • Certain registers are used as dedicated registers and programmers are not expected to use them for any other purpose.
- Registers R14 through R17 are used for storing return address from interrupts, sub-routines, traps, and exceptions in that order. Subroutines are called using the branch and link instruction, which saves the current Program Counter (PC) onto register R15.
- Small data area pointers are used for accessing certain memory locations with 16 bit immediate value. These areas are discussed in the memory model section of this document. The read only small data area (SDA) anchor R2 (Read Only) is used to access the constants such as literals. The other SDA anchor R13 (Read-Write) is used for accessing the values in the small data read write section.
- Register R1 is used to store the value of the stack pointer and is updated on entry and exit from functions.
Register R18 is used as a temporary register for assembler operations.

## Slide 15: Outline
What is MB-GCC and How is It Made Up?
MicroBlaze Application Binary Interface
Optimization & Debugging Options
Runtime Routines & The Object File
Interrupt Handling
Summary

## Slide 16: Optimization
The Option -O <n>:
(where n = 0,1,2,3, specifies the optimisation level)
  Compiles your program with optimisation turned on
  Reduces the size of your executable
  Reduces the number of cycles it needs to execute
The Option -mxl-gp-opt:
  Use the small data area anchors
  Optimize for performance and size
Notes: Once you are satisfied that your program is correct, recompile your program with optimisation turned on. This will reduce the size of your executable and reduce the number of cycles it needs to execute. This is achieved by the following:
mb-gcc -O3 file1.c file2.c
If the memory location requires more than 32K, the load/store operation would require two instructions. MicroBlaze ABI offers two global small data areas, which can contain up to 64K bytes of data each. Any memory location within these areas can be accessed using the small data area anchors and a 16-bit immediate value, hence needing only one instruction for load/store to the small data area. This optimisation can be turned ON with the -mxl-gp-opt command line parameter. Variables of size lesser than a certain threshold value are stored in these areas. The value of the pointers is determined during linking. The threshold value can be changed using the -Gn option.
The compiler stores certain data in the small data area of the code. Any global variable, which is equal to or lesser than 8 bytes, will be stored in the small data area of the read-write or read only section. This threshold value of 8 bytes could be changed using the -Gn option in the command line.

## Slide 17: Debugging Options
Debugging using hardware:
  Software intrusive
  Needs to connect to the hardware platform
  Create your application executable using the command:
  mb-gcc -g -xl-mode-xmdstub file1.c file2.c
Notes: You can debug your program on a board, which has a Xilinx FPGA loaded with your hardware bitstream.
You will need to create your application executable using the following command:
mb-gcc -g -xl-mode-xmdstub file1.c file2.c
This command creates the MicroBlaze executable a.elf, linked with the C runtime library crt1.o and starting at physical address 0x400 and with debugging information that can be read by mb-gdb, the MicroBlaze GNU debugger. You must run Platform Generator with the -mode xmdstub option. This initialises the Local Memory (LM) with the xmdstub executable. Next, load the bitstream representing your design onto your FPGA.

## Slide 18: Debugging Options
Debugging using a simulator (XMD ISS, MB-GDB):
  Software non-intrusive
  Compile programs using the command:
  mb-gcc -g file1.c file2.c
Notes: If you want to debug your code using a simulator, compile programs using the command: mb-gcc -g file1.c file2.c
This command creates the MicroBlaze™ executable file, a.elf with debugging information that can be accessed by mb-gdb.
Xilinx provides two ways to debug programs in simulation.
1. Cycle-accurate simulator in XMD
2. Simple ISA simulator in mb-gdb
mb-gdb is the GNU debugger used to debug your MicroBlaze software.

## Slide 19: MB-GCC Main Options
Option
Description
-xl-mode-xmdstub
-xl-mode-executable
-xl-mode-bootstrap-reset
-mxl-stack-check
-mxl-soft-mul
-mno-xl-soft-mul
-xl-mode-bootstrap
Intrusive hardware debugging on the board.Should be used only with xmdstub downloaded on to MicroBlaze
Generate code, which can be downloaded using the boot strap loader
Default mode for compilation.
Same as bootstrap mode, but in this case, on reset, the control is transferred to user program instead of the boot stub.
Do not use software multiplier. Compiler generates “mul” instructions.
Use software multiplier. Use this option when hardware multiplier is not present in the device. By default this option in turned ON.
Generates code for checking stack overflow.
-xl-mode-xilkernel
If you use the xilkernel module, all the programs should be compiled with this option.
-mxl-gp-opt
Use small data area anchors. Optimization for performance and size.
-mxl-barrel_shift
Use barrel shifter. Use this option when the MicroBlaze Core includes a barrel.
Notes: The mb-gcc compiler for the Xilinx MicroBlaze soft processor introduces some new options as well as modifications to certain options supported by the GNU compiler tools. The new and modified options are summarized in the above table.
-xl-mode-xilkernel:
A kernel consisting of few key RTOS features is provided with the EDK tools. All the programs compiled to work with the kernel should have the above option.
Caution! mb-gcc will signal fatal error if more than one mode of execution is supplied on the command line.
Multiplication using software libraries is the default mode for compilation if the FPGA target is a Virtex™-II and Code portability across different FPGA architectures (Virtex based with no embedded multipliers) is not a requirement, then the option -mno-xl-soft-mul switch should be passed to the MB-GCC to benefit from MUL instructions that could be executed by the MicroBlaze ALU and then speed up Application Code execution.

## Slide 20: MB-GCC Main Options
Option
Description
-save-temps
-O <n>
-Wa, <option>
--help
-Wp, <option>
-Wl, <option>
-lm
Should be specified for programs that access libm math functions.
Pass comma-separated <options> on to the assembler
Pass comma-separated <options> on to the preprocessor
Pass comma-separated <options> on to the linker
Store intermediate files
Display a short listing of options.
Specify Optimization level n = 0,1,2,3
-B
-L
-I
-v
-o
Add <directory> to the C-run time library search paths
Add <directory> to header search path
Display the programs invoked by the compiler
Place the output in <file>
Add <directory> to library search path
-E
-c
-g
-S
Preprocess only; Do not compile, assemble and link (Generates .i file)
Compile only; Do not assemble and link (Generates .s file)
Compile and Assemble only; Do not link (Generates .o file)
Add debugging information for gdb to the final executable
Notes: The -lm switch should be the last option passed to the mb-gcc in the command line!

## Slide 21: Outline
What is MB-GCC and How is It Made Up?
MicroBlaze Application Binary Interface
Optimization & Debugging Options
Runtime Routines & The Object File
Interrupt Handling
Summary

## Slide 22: Initialisation Files
Initialisation can be done using one of the four C runtime routines:
crt0.o: Used in Executable mode
crt1.o: Used in Debug mode
crt2.o: Used in Bootstrap mode with control back to the boot stub after a Reset
crt3.o: Used in Bootstrap mode with control back to the user program after a Reset
Notes: The final executable needs certain registers such as the small data area anchors (R2 and R13) and the stack pointer (R1) to be initialized. These initialisation files are distributed with the MicroBlaze™ Development Kit. In addition to the precompiled object files, source files are also distributed in order to help you make your own changes as per your requirements. Initialisation can be done using one of the four C runtime routines:
crt0.o: This initialisation file is to be used for programs that are to be executed standalone, i.e., without xmd.
crt1.o : This file is located in the same directory and should be used when the xmd debugger is to be present in the system.
crt2.o : In case of programs used with the boot-loader, crt2.o is used as the initialisation file. The boot loader is used to load the program at runtime using the boot stub.
crt3.o : The source for crt2.o and crt3.o is the same as the functionality is the same except for the behavior on a reset. In crt3.o, address location 0x0 is overwritten, such that on a reset, the control is transferred to the user program instead of the boot stub. These files are described in detail in the MicroBlaze ABI documentation. The source for initialisation file can be changed as per the requirements of the project. These changed files have to be then assembled to generate an object file (.o format). To refer to the newly created object files instead of the standard files, use the -B <directory-name> command line option while invoking mb-gcc.

## Slide 23: The Object File
.text: This section contains executable code.
.rodata: This section contains read-only data of size more than 8 bytes (default)
.sdata2: This section contains small read-only data (size less than 8 bytes)
.data: This section contains read-write data of size more than 8 bytes (default)
Notes: .text: This section contains executable code. This section has the x (executable), r (read-only) and i (initialized) flags.
.rodata: This section contains read-only data of size more than 8 bytes (default). The size of the data put into this section can be changed with an mb-gcc -G option. All data in this section is accessed using absolute addresses. This section has the r (read-only) and the I (initialized) flags. For more details refer to the MicroBlaze ABI documentation.
.sdata2: This section contains small read-only data (size less than 8 bytes). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed with reference to the read-only small data anchor. This ensures that all data in the .sdata2 section can be accessed using a single instruction (a preceding imm instruction will never be necessary). This section has the r (read-only) and the i (initialized) flags. For more details refer to the MicroBlaze ABI documentation.
.data: This section contains read-write data of size more than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed using absolute addresses. This section has the w (read-write) and the I (initialized) flags.

## Slide 24: The Object File
.sdata: This section contains small read-write data of size less than 8 bytes (default)
.sbss: This section contains small un-initialized data of size less than 8 bytes (default)
.bss: This section contains un-initialized data of size more than 8 bytes (default)
Notes: .sdata: This section contains small read-write data of size less than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed with reference to the read-write small data anchor. This ensures that all data in the .sdata section using a single instruction. (A preceding imm instruction will never be necessary). This section has the w (read-write) and the i (initialized) flags.
.sbss: This section contains small un-initialized data of size less than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. This section has the w (read-write) flag.
.bss: This section contains un-initialized data of size more than 8 bytes (default). The size of the data going into this section can be changed with an mb-gcc -G option. All data in this section is accessed using absolute addresses. The stack and the heap are also allocated to this section. This section has the w (read-write) flag. The linker script describes the mapping between all the sections in all the input object files and the output executable file.

## Slide 25: The Object File
Section Description
.text Text Section
.rodata Read-Only Data Section
.sdata2 Small Read-Only Data Section
.data Read-Write Data Section
.sdata Small Read-Write Data Section
.sbss Small Un-initialized Data Section
.bss Un-initialized Data Section
Sectional layout of an object or executable file

## Slide 26: Minimal Linker Script
Could the memory be mixed: LMB + OPB + External?
  Yes
Could the memory be non-contiguous?
  Yes
Notes: If your LMB, OPB, and External Memory do not occupy contiguous areas of memory, you can use a minimal linker script to define your memory layout.

## Slide 27: Minimal Linker Script Example
/*
* Define the memory layout, specifying the start address and size of the
* different memory regions. The ILMB will contain only executable code (x),
* the DLMB will contain only initialized data (i), and the DOPB will contain
* all other writable data (w). Note that all sections of all your input
* object files must map into one of these memory regions. Other memory types
* that may be specified are "r" for read-only data.
*/
MEMORY
{
ILMB (x) : ORIGIN = 0x0, LENGTH = 0x1000
DLMB (i) : ORIGIN = 0x2000, LENGTH = 0x1000
DOPB (w) : ORIGIN = 0x8000, LENGTH = 0x30000
}
Notes: The slide shows a minimal linker script that describes the memory regions only, and uses the default (built-in) linker script for everything else.
This script specifies that the ILMB memory will contain all object file sections that have the x flag, the DLMB will contain all object file sections that have the I flag, and the DOPB will contain all object file sections that have the w flag. An object file section that has both the x and the i flag (.e.g., the .text section) will be loaded into ILMB memory because this is specified first in the linker script. Refer to the Object-file Sections section of this document for more information on object file sections and the flags that are set in each. Your source files can now be compiled by specifying the minimal linker script as though it were a regular file, e.g.,
mb-gcc <minimal linker script> file1.c file2.c
Remember to specify the minimal linker script as the first source file. If you want more control over the layout of your memory, e.g., if you want to split up your .text section between ILMB and IOPB, or if you want your stack and heap in DLMB and the rest of the .bss section in DOPB, you will need to write a full-fledged linker script.

## Slide 28: Minimal Linker Script Example
MEMORY
{
ILMB (x) : ORIGIN = 0x0, LENGTH = 0x1000
DLMB (i) : ORIGIN = 0x2000, LENGTH = 0x1000
DOPB (w) : ORIGIN = 0x8000, LENGTH = 0x30000
}
MicroBlaze System Memory MAP
0x0
0x1000
ILMB(x) Region
DLMB(i) Region
0x3000
0x2000
ILMB(x) Region
DLMB(i) Region
0x8000
0x38000
ILMB(x) Region
DOPB(w) Region
0xFFFFFFF

## Slide 29: The Linker Script
If you choose to write a linker script, you must do the following:
Allocate space in the .bss section for stack and heap
Ensure that he _SDA2_BASE_ variable points to the center of the .sdata2 area
Ensure that _SDA2_BASE_ is aligned on a word boundary
Ensure that the .sdata and the .sbss sections are contiguous
If you are not using the rom monitor, ensure that crt0 is always loaded into memory address zero
Notes: Note that if you choose to write a linker script, you must do the following to ensure that your program will work correctly:
• Allocate space in the .bss section for stack and heap. Set the _heap variable to the beginning of this area, and the _stack variable to the end of this area. See the .bss section in the script Example.
• Ensure that the _SDA2_BASE_ variable points to the center of the .sdata2 area and that _SDA2_BASE_ is aligned on a word boundary.
• Ensure that the .sdata and the .sbss sections are contiguous, the _SDA_BASE_ variable points to the center of this section, and _SDA_BASE_ is aligned on a word boundary.
• If you are not using the rom monitor, ensure that crt0 is always loaded into memory address zero. mb-gcc ensures that this is the first file specified to the loader, but the loader script needs to ensure that it gets loaded at address zero. See the .text section in the example Appendix-2 to see how this is done.

## Slide 30: Linker Script Example
/*
* Define the memory layout, specifying the start address and size of the
* different memory regions.
*/
MEMORY
{
LMB : ORIGIN = 0x0, LENGTH = 0x1000
OPB : ORIGIN = 0x8000, LENGTH = 0x5000
}
/*
* Specify the default entry point to the program
*/
ENTRY(_start)
/*
* Define the sections, and where they are mapped in memory
*/
SECTIONS
{
/*
* Specify that the .text section from all input object files will be placed
* in LMB memory into the output file section .text Note that mb-gdb expects
* the executable to have a section called .text
*/

## Slide 31: Linker Script Example
.text : {
/* Uncomment the following line to add specific files in the opb_text */
/* region */
/* *(EXCLUDE_FILE(file1.o).text) */
/* Comment out the following line to have multiple text sections */
*(.text)
} >LMB
/* Define space for the stack and heap */
/* Note that variables _heap must be set to the beginning of this area */
/* and _stack set to the end of this area */
. = ALIGN(4);
_heap = .;
.bss : {
_STACK_SIZE = 0x400;
. += _STACK_SIZE;
. = ALIGN(4);
} >LMB
_stack = .;
/* */
/* Start of OPB memory */
/* */
.opb_text : {
/* Uncomment the following line to add an executable section into */
/* opb memory */
/* file1.o(.text) */
} >OPB

## Slide 32: Linker Script Example
. = ALIGN(4);
.rodata : {
*(.rodata)
} >OPB
/* Alignments by 8 to ensure that _SDA2_BASE_ on a word boundary */
. = ALIGN(8);
_ssrw = .;
.sdata2 : {
*(.sdata2)
} >OPB
. = ALIGN(8);
_essrw = .;
_ssrw_size = _essrw - _ssrw;
_SDA2_BASE_ = _ssrw + (_ssrw_size / 2 );
. = ALIGN(4);
.data : {
*(.data)
} >OPB
/* Alignments by 8 to ensure that _SDA_BASE_ on a word boundary */
/* Note that .sdata and .sbss must be contiguous */
. = ALIGN(8);
_ssro = .;
.sdata : {
*(.sdata)
} >OPB

## Slide 33: Linker Script Example
. = ALIGN(4);
.sbss : {
*(.sbss)
} >OPB
. = ALIGN(8);
_essro = .;
_ssro_size = _essro - _ssro;
_SDA_BASE_ = _ssro + (_ssro_size / 2 );
. = ALIGN(4);
.opb_bss : {
*(.bss) *(COMMON)
} > OPB
. = ALIGN(4);
_end = .;
}

## Slide 34: Outline
What is MB-GCC and How is It Made Up?
MicroBlaze Application Binary Interface
Optimization & Debugging Options
Runtime Routines & The Object File
Interrupt Handling
Summary

## Slide 35: MicroBlaze Interrupt Handling
Main Function:
….
Instruction 1;
Instruction 2;
…
Instruction i;
Instruction i+1;
…
Instruction n;
End of Main;
1- Interrupt Request
Stop execution of Instruction i
Branch to the ISR( )
Disable Interrupts
Saving of the Registers in the Stack
Execution of the ISR( ) associated Instructions
Restoring the saved values from the stack
Enable Interrupt
Return to the address of Instruction i in the Main function
2- Jump to the Interrupt Service Routine: ISR( )
4- Return to the Main Function
3- House Keeping and Execution of the ISR( )
Notes: The MicroBlaze™ soft processor has one interrupt signal, which is enabled in the MSR register. The IMM instruction (Immediate) will temporarily disable interrupts. Interrupt latency depends upon your system. If there is no interrupt controller, the latency on interrupts is 4 clock cycles -- 1 for detecting, and 3 for branching to the interrupt routine. If an interrupt controller exists, there is additional latency while the interrupt controller ISR saves registers, finds out which peripheral initiated the interrupt, and determines priority.
The saving of the internal MicroBlaze registers is part of Interrupt Service Routine. There is no need to save all of them (this is automated in the EDK). In the MSS (Microprocessor Software Specification file), the user will tag a routine as an ISR with an “_int_handler” attribute. Libgen and mb-gcc save all registers, correctly returning from the ISR while only saving the registers modified during the routine.
Interrupt latency depends on the complexity of the interrupt handler (which is simply program code). You can use GDB/XMD to target either the ISS or the real hardware to obtain a cycle count (number of processor clock cycles) for how long it takes to execute your interrupt handler (set one break point before, one after, select "Run", and you will see the cycle count). Multiply this by the cycle period of the processor system (1/Fmax), and you will have the interrupt handler latency in wall clock time.

## Slide 36: The Stack
Data structure for storing items that are to be accessed in last-in first-out order
The MicroBlaze™ stack is used to store:
  Function call
  Register saving
  Local variables
MicroBlaze instruction set does not support stack operations (no pop and push instructions)
Stack operations are handled by software application
MicroBlaze stack size could be modified at compile time by using a linker switch
Notes: The _STACK_SIZE_ option to mb-gcc specifies the total memory allocated to stack and heap.
The stack is used for function calls, register saves, and local variables. All calls to malloc allocate memory from heap. The stack pointer initially points to the bottom (high end) of memory, and grows toward low memory while the heap pointer starts at low memory and grows towards high memory. The size of the heap cannot be increased at runtime. The return value of malloc must always be checked to ensure that it could actually allocate the memory requested.

## Slide 37: Stack Convention
Notes: The stack conventions used by MicroBlaze™ soft processor are detailed in the slide. The shaded area in the table denotes a part of the caller function’s stack frame, while the unshaded area indicates the callee function’s frame. The ABI conventions of the stack frame define the protocol for passing parameters, preserving non-volatile register values and allocating space for the local variables in a function. Functions that contain calls to other subroutines are called as non-leaf functions.
These non-leaf functions have to create a new stack frame area for its own use. When the program starts executing, the stack pointer will have the maximum value. As functions are called, the stack pointer is decremented by the number of words required by every function for its stack frame. The stack pointer of a caller function will always have a higher value as compared to the callee function.

## Slide 38: Stack Convention
Notes: Consider an example where Func1 calls Func2, which in turn calls Func3. The stack representation at different instances is depicted in the figure above.
After the call from Func 1 to Func 2, the value of stack pointer (SP) is decremented. This value of SP is again decremented to accommodate the stack frame for Func3.
On return from Func 3 the value of stack pointer is increased to its original value in the function, Func 2.

## Slide 39: Outline
What is MB-GCC and How is It Made Up?
MicroBlaze Application Binary Interface
Optimization & Debugging Options
Runtime Routines & The Object File
Interrupt Handling
Summary

## Slide 40: Review Questions
List the three main components of the mb-gcc
What are the different optimisation options offered by mb-gcc?
Describe the different debugging possibilities available for the MicroBlaze™ firmware
List and describe the different runtime routines of the MicroBlaze processor
List and describe the different sections of the MicroBlaze object or executable file
What is a linker script and could it be modified by the user?
Which register is used to store the returning address of the MicroBlaze PC after an interrupt service routine?

## Slide 41: Answers
List the three main components of the mb-gcc?
  The MicroBlaze GNU Cross Compiler top level is mb-gcc.exe and it calls the following three main components:
    1- cc1.exe - The compiler
    2- mb-as.exe - The assembler
    3- mb-ld.exe - The linker loader

## Slide 42: Answers
What are the different optimisation options offered by mb-gcc?
  The option -O <n>
  (where n = 0,1,2,3, specifies the optimisation level)
  The option -mxl-gp-opt
Describe the different debugging possibilities available for the MicroBlaze™ firmware?
  Debugging using hardware
  Debugging using a simulator:
  1. Cycle-accurate simulator in XMD
  2. Simple ISA simulator in mb-gdb

## Slide 43: Answers
List and describe the different runtime routines of the MicroBlaze™ processor?
  The MicroBlaze initialisation can be done using one of the four C runtime routines:
  1- crt0.o: Used in Executable mode
  2- crt1.o: Used in Debug mode
  3- crt2.o: Used in Bootstrap mode with control back to the boot stub after a reset
  4- crt3.o: Used in Bootstrap mode with control back to the user program after a reset

## Slide 44: Answers
List and describe the different sections of the MicroBlaze™ object or executable file?
  The sectional layout of a MicroBlaze object or executable file is as follow:
  1- .text: Text section
  2- .rodata: Read-only data section
  3- .sdata2: Small read-only data section
  4- .data: Read-write data section
  5- .sdata: Small read-write data section
  6- .sbss: Small un-initialized data section
  7- .bss: Un-initialized data section

## Slide 45: Answers
What is a linker script and could it be modified by the user?
  It is a script file used by the compiler (linker) to define the memory layout of the object or executable file where the start address and the size of the different memory regions are specified. When the memory (LMB + OPB RAM + External) is non-contiguous, the user should provide a custom linker script defining the memory MAP of the different sections of his object or executable file, according to how his physical memory is mapped
Which register is used to store the returning address of the MicroBlaze PC after an interrupt service routine?
  <R14>

## Slide 46: Summary
MB-GCC is the compiler used to transform your “C” source code into a MicroBlaze™ executable format
MB-GCC offers optimization and debugging options for use during the development of your MicroBlaze firmware
Four different runtime routines are available with the MB-GCC
The linker script is the file defining the sectional layout of your object or executable file