## Slide 1: MicroBlaze Buses

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the differences between the Local Memory and On-Chip Peripheral Buses (LMB and OPB)
Describe the signals that make up the OPB and LMB
Describe the function of an arbiter and multiple-master systems

## Slide 3: Outline
The Local Memory Bus
The On-Chip Peripheral Bus
The Arbiter
Summary

## Slide 4: Local Memory Bus
Xilinx-specific Bus Architecture
Synchronous
Fast bus interface specifically for on-chip block RAMs
No support for multiple masters
Available on the Data and Instruction sides of the MicroBlaze™ soft processor core
  DLMB
  ILMB
Notes: The local memory bus is a Xilinx-specific bus for connecting on-chip block RAMs. The bus is as fast as it is simple and limited in the number of control signals.

## Slide 5: LMB Operation
Active on the rising edge
Fast bus specific to internal Xilinx block RAMs
Generic Read
Generic Write
Notes: Here we can see a generic read and write transaction on the Local Memory Bus. The Address Strobe (AS) qualifies the address and data lines. The slave then completes the transaction with the ready flag.
The data bus is unidirectional, and so has separate write and read data buses. This fits well with the block RAMs inside the FPGA.

## Slide 6: LMB Implementation
Xilinx Block Ram
WE
DIN
Q
D
DOUT
Addr
Ready
Byte_enable(0)
Data_read
AS
Write_strobe
Reset
Clk
addr
Data_write
WE
x4 (4 Byte Enables)
Byte_enable(1)
Notes: The diagram above illustrates a possible implementation for block RAMs on the Local Memory Bus.
As the block RAM can read and write data in a clock cycle, the ready signal is simply the AS signal delayed by one clock cycle.
The write enable is activated with the byte-enable and the write strobe.
Please note that only one byte-enable is shown here. In the actual implementation of the LMB, there would be four, or multiples of four block rams, so that all four byte-enables are serviced.

## Slide 7: Outline
The Local Memory Bus
The On-Chip Peripheral Bus
The Arbiter
Summary

## Slide 8: On-Chip Peripheral Bus
IBM CoreConnect™ bus structure
Synchronous
  All masters and slaves are synchronous to the OPB_CLK
32-bit address bus, 32-bit data bus
  Byte enables, to support 8, 16 and 32-bit transactions
OR-gate structure - no internal 3-state drivers
Multiple master support
  Requires an arbiter
Notes: The On-Chip peripheral bus is used to connect peripherals to the MicroBlaze system. This is a standard bus interface defined by IBM and is synchronous to the bus clock. The data bus uses OR logic rather than 3-state to interface peripherals, and so is ideally suited to embedded systems.
The bus enables multiple masters when used with a bus arbiter.

## Slide 9: OPB* with 1 Slave, 1 Master
OPB Master ‘M0’
Slave ‘0’
M0_ABUS
M0_DBUS
OPB_DBUS
SL0_DBUS
Read from Slave
Write to Slave
Here we can see the OR-gate structure in use. When the OPB Master is reading data from the Slave, its DBUS output is set to ‘0’, and the slave DBUS is activated. When writing, the slaves DBUS is inactive, and the Master data reflects on the output of the OR gate.
*Control signals not shown
Notes: The most simple OPB system has one master and one slave. We can see in the diagram, above, the data path constructed around the OR gate.
The control signals are not shown on this diagram for clarity, but shall be discussed in more detail on a later slide.

## Slide 10: OPB* with Multiple Slaves
OPB Master ‘M0’
Slave ‘1’
Slave ‘2’
Slave ‘3’
Slave ‘0’
SL0_DBUS
SL1_DBUS
SL2_DBUS
SL3_DBUS
M0_ABUS
OPB_DBUS
OPB_ABUS
M0_DBUS
*Control signals not shown
As we add more slaves, the OR gate gets bigger to form the data bus
Q. How could more slaves affect the maximum speed of the system?
Notes: With multiple slaves there are more data paths, and so the OR gate structure becomes larger. We can see in the diagram, above, that there is in fact one input to the OR gate for each slave and the master.
Note: The Microblaze hardware does also have provision for separate read and write buses. This would decrease the combinatorial path delay and shall be utilized in a later version of the EDK tools.

## Slide 11: Basic OPB Transaction
Valid Address
Valid Data
The Master requests the bus
The Master is Granted Access
The transaction takes place
The Slave specifies the end of the transaction
*
* Combinatorial Grant signal shown (This could also be registered)
Notes: The waveform, above, illustrates a basic OPB transaction. The master requests the bus, and this request is granted. It should be noted that the grant signal can be combinatorial, as shown above, for less latency, or registered for more pipelining.
Once bus access is granted, the transaction takes place.
The slave signals the end of the transaction by asserting the XFERACK signal (Transfer Acknowledged) for one clock cycle.
The OPB specifications from IBM indicate that if the XFERACK signal is not asserted within 16 clock cycles, the arbiter should time-out the bus unless a timeout suspension signal is asserted.

## Slide 12: On-Chip Peripheral Bus
The OPB also supports multiple masters
  Only one master has access to the bus at a time
  An arbiter is required in order to grant access
  All OPB peripherals are available to both masters

## Slide 13: OPB* with Multiple Masters
*Control signals not shown
OPB Master ‘M0’
Slave ‘1’
Slave ‘2’
Slave ‘3’
Slave ‘0’
OPB Master ‘M1’
Arbiter
SL0_DBUS
SL1_DBUS
SL2_DBUS
SL3_DBUS
M0_ABUS
M1_ABUS
OPB_DBUS
OPB_ABUS
M1_DBUS
M0_DBUS
OPB_M0GRANT
OPB_M1GRANT
M1_REQUEST
M0_REQUEST
OR-Gate Bus Structure
Notes: Here we can see a system with more than one master. In order to stop more than one master from accessing the bus at the same time, an Arbiter is required to control bus ownership. The function of an arbiter shall be discussed later.
As can be seen, an OR gate has been applied to the address bus as well as the data bus. The size of the OR bus gate is equal to the number of masters on the system.
The arbiter is not automatically added to the system; the user must declare it in the .mhs file.

## Slide 14: Outline
The Local Memory Bus
The On-Chip Peripheral Bus
The Arbiter
Summary

## Slide 15: OPB Arbiter
Allows more than one master on the same bus
  Priority, or Round-Robin schemes for ‘fair’ access to the bus
OPB_CLK
M0_request
M1_request
M2_request
M3_request
OPB_M0GRANT
OPB_M1GRANT
OPB_M2GRANT
OPB_M3GRANT
OPB_xferack
OPB_CLK
M0_request
M1_request
M2_request
M3_request
OPB_M0GRANT
OPB_M1GRANT
OPB_M2GRANT
OPB_M3GRANT
OPB_xferack
Round-robin Arbitration
Priority Arbitration
Notes: The role of the arbiter is to control access to the bus. There are many different priority algorithms that can be used for this. However, the most common of these are round-robin and priority arbitration, as illustrated above.
In a round-robin scheme, each master has equal priority in the system, and so the arbiter allocates the bus with this equal priority.
In a priority system, each master has a priority and so the highest priority master can get access to the bus, even when another master is requesting it. It should be noted that a priority scheme can lead to ‘bus starvation’, the situation that a high-priority master prevents another lower-priority master access to the bus for an extended period of time. Round-robin or custom arbiter peripherals can prevent this situation, if required.

## Slide 16: Outline
The Local Memory Bus
The On-Chip Peripheral Bus
The Arbiter
Summary

## Slide 17
Skills Check

## Slide 18: Review Questions
What is the function of the LMB?
What is the function of the OPB?
How many masters can be on the LMB?
If I have an OPB with 2 masters, and 6 slaves, how wide would the data or gate be?
What is the function of an arbiter?

## Slide 19: Answers
What is the function of the LMB?
  It is a high-speed Local Memory Bus specifically designed for On-Chip Block RAMs
What is the function of the OPB?
  The OPB is the On-Chip Peripheral Bus specification for connecting together master and slave peripherals. It has an Or-gate structure to avoid 3-state buses.
How many masters can be on the LMB?
  The LMB is a single master bus

## Slide 20: Answers
If I have an OPB with 2 masters, and 6 slaves, how wide would the data or gate be?
  The OR gate structure requires one input per bus-driver. This would equate to 2 + 6 = 8 inputs
What is the function of an arbiter?
  An arbiter receives requests and generates grants for masters to gain access to the bus. Only one master is allowed to access the bus at any one time

## Slide 21: Summary
The Local Memory Bus (LMB) is a fast bus, specifically for Xilinx block RAMs
The On-Chip Peripheral Bus (OPB) is an IBM standard bus for connecting peripherals
An arbiter manages the bus on a multiple master system and can have one of many priority schemes

## Slide 22: OPB – Quick Reference

## Slide 23: LMB – Quick Reference