## Slide 1: MicroBlaze Architecture

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the MicroBlaze™ core architecture
Describe the six MicroBlaze core configurations
Explain MicroBlaze interrupts

## Slide 3: Introduction
The MicroBlaze™ soft processor core is a RISC Processor
RISC: Reduced Instruction Set Computer
  Software concept architecture
  Simple instructions
  Small instruction set
  Instructions have the same length
  Instructions execute in a single processor clock cycle
  Focus on simple Processor Core => High Clock Speed

## Slide 4: Introduction
The MicroBlaze™ soft processor is also based on the Harvard architecture
Harvard architecture:
  Hardware concept architecture
  Separate data and instruction buses
  Both an Instruction and a Datum can be fetched in a single clock cycle
  Execution of an instruction every clock cycle even if the instruction needs data

## Slide 5: Outline
MicroBlaze Core Architecture
MicroBlaze Core Configurations
Exceptions and Interrupts

## Slide 6: MicroBlaze Core Architecture
The MicroBlaze™ soft processor core is built from the FPGA logic resources
MicroBlaze core implementation takes around 450 slices
Main differences between the Virtex™ and the Virtex™ -II FPGAs implementations are:
  Usage of the Virtex-II embedded multipliers
  The register file is built from:
    A primitive RAM32x1d in the Virtex-II FPGA
    Two primitives RAM16x1d in the Virtex-based FPGAs
The implementation of the MicroBlaze core in Spartan™ -II FPGAs is identical to the Virtex FPGAs

## Slide 7: MicroBlaze Core Architecture
Instruction-side bus interface
Instruction
Buffer
Program
Counter
Instruction Decode
Data-side bus interface
Register File
32 x 32b
Shift/
Logical
Add/Sub
Mult
ILMB
DLMB
IOPB
DOPB
Notes: We can see the major blocks within the MicroBlaze processor: the Bus Interfaces, the Instruction Buffer, the ALU, and the Register File. We shall see how the MicroBlaze processor handles the execution of the Instructions. The Instruction Buffer (the pre-fetch buffer) does NOT add any extra clock cycles. The pre-fetch buffer is part of the pipeline -- it is better described as an elastic buffer between two pipe stages that can hold 0-16 values.
The MicroBlaze soft processor has an orthogonal ISA: (Instruction Set Architecture). This means that all instructions can work on any registers. If you had instructions that only could work on register 1 or 15, the code wouldn't be orthogonal.
The MicroBlaze core gives the option of including a Barrel Shifter in the core. If this feature is needed, then the following attribute needs to be specified in the MHS file within the MicroBlaze core section:
PARAMETER C_USE_BARREL = 1

## Slide 8: MicroBlaze Core Architecture
The MicroBlaze™ core is a RISC processor
Each instruction is word aligned
The MicroBlaze core has two type of instructions:
  Instruction type A
  Instruction type B
Notes: All Loads need at least 2 clock cycles. Stores could take 1 clock cycle for writing into LMB memory. All OPB accesses need extra clock cycles dependent on the OPB peripheral.
In Virtex-II devices, multiplication takes 3 clock cycles, using the dedicated hardware multiplier. All other instructions take 1 clock cycle.
Dedicated multiplier blocks are available in Virtex-II devices, and the MicroBlaze core takes full advantage of these hard cores in Virtex-II MicroBlaze implementations.
32-bit x 32-bit multiplications in the MicroBlaze soft processor running on Virtex-II device:
If the input and resultant data types are of type "long" [32 bit], then the multiply instruction takes 3 clock cycles. This multiply takes full advantage of the dedicated multiplier block.
64-bit x 64-bit multiplications in the MicroBlaze soft processor running on Virtex-II device:
If the input and resultant data types are of type "long long" [64 bit], then the multiply instruction will take approximately 100 clock cycles. In devices with Virtex-based architectures (Virtex, Virtex-E, Spartan-II, Spartan-IIE), these multipliers are not available. As a result, all multiply instructions (including long long) in these versions of the MicroBlaze soft processor will be software multiplies. These software multiplies take a few thousand clock cycles to complete.

## Slide 9: MicroBlaze Core Architecture
Type A instruction example:
ADD Rd,Ra,Rb // Rd := Ra + Rb
0b000000 Rd Ra Rb
The values of Rd, Ra, Rb are assigned at compile time by the Compiler according to the Registers File Usage at this particular instruction of the code

## Slide 10: MicroBlaze Core Architecture
Type B instruction example:
ADDI Rd,Ra,Imm // Rd := s(Imm) + Ra
The values of Rd, Ra are assigned at compile time by the Compiler according to the Registers File Usage at this particular instruction of the code
0b001000 Rd Ra

## Slide 11: MicroBlaze Core Architecture
The MicroBlaze™ core is a Harvard processor
The MicroBlaze core is a big-endian processor
The MicroBlaze core has 32 general purpose registers: R0 to R31
  R0 is always equal to 0
The MicroBlaze core has two special purpose registers:
  MSR: Machine State Register
  PC: Program Counter
Each register is 32-bit wide
Notes: MicroBlaze processor aims to execute one instruction per clock cycle except for:
- Load/Store - 2 clock cycles
- Multiply - 3 clock cycles
- Branches - 3 clock cycles; (can be 1 clock cycle when pre-scheduled)
The ALU will perform operations in a single cycle for all the other instructions. However, the ALU operation does not represent everything that needs to be done in order to execute. The instruction needs to be fetched, decoded and then executed.
MicroBlaze itself is always big-endian; it only supports big-endian storage device and fetching units. MicroBlaze does not have a register or attribute to store the endianness. Therefore, the user needs to design big-endian and convert data alignment.

## Slide 12: MicroBlaze Core Architecture
Three stage pipeline for the instruction data path
  IF Instruction Fetch
  OF Operand Fetch
  EX Execute
There is no write-back stage
Notes: The MicroBlaze processor breaks the execution process of an instruction into three stages.
These stages are called a “pipeline” through which instructions flow. At any one time (No Jump) there will be three instructions “in flight”: one being fetched from the instruction memory; one being decoded; and one being executed.
Although pipelining allows the processor to run faster by splitting the process of fetching an instruction and then executing it into stages, it can cause problems such as: Load delay slot and Branch delay slot.

## Slide 13: MicroBlaze Core Architecture
The MicroBlaze™ soft processor core has two different bus structures
  LMB: Local Memory Bus
  OPB: IBM CoreConnect On-Chip Peripheral Bus
LMB connects only to the on-chip block RAMs
LMB access latency is one clock cycle per transaction
OPB is the main bus to connect the MicroBlaze core and its peripherals
OPB access latency depends on the type of peripheral being addressed
Notes: The on-chip memory block RAMs that could be connected to the LMB is FPGA architecture dependant:
A maximum of 64 KB for the Virtex-II/Pro FPGA families
A maximum of 16 KB for the Virtex/E and Spartan-II/E FPGA families
On-chip memory size could be customized by the designer according to his need, the allowed sizes are:
2 KB, 4 KB, 8 KB, and 16 KB for the Virtex/E & the Spartan-II/E families
8 KB, 16 KB, 32 KB, and 64 KB for the Virtex-II/Pro families
LMB Base address must start at Offset [0x00000000] in the MicroBlaze memory MAP.

## Slide 14: MicroBlaze Core Architecture Questions
What is a RISC architecture?
What is the main characteristic of a Harvard architecture?
On which architecture is MicroBlaze™ processor core based?
How big is the MicroBlaze registers file?
How many types of instructions does the MicroBlaze instruction set have? How long are they?
What are the MicroBlaze bus interfaces?

## Slide 15: MicroBlaze Core Architecture Answers
What is a RISC architecture?
  Reduced Instruction Set Computer
  Software concept processor architecture with simple instructions, small instruction set where instructions have the same length and execute in a single clock cycle
What is the main characteristic of a Harvard architecture?
  It has separate instruction and data buses and could fetch an instruction and a datum simultaneously
On which architecture is MicroBlaze™ processor core based?
  A Harvard processor based on RISC architecture
How big is the MicroBlaze registers file?
  Has 32 general purpose registers [R0 to R31], a dedicated Program Counter PC Register, and the Machine Status Register MSR

## Slide 16: MicroBlaze Core Architecture Answers
How many types of instructions does the MicroBlaze™ instruction set have? How long are they?
  MicroBlaze instruction set has Two type of instructions:
    Instruction type A: opcode|DR|SRA|SRB|
    Instruction type B: opcode|DR|SR|Imm
  Each instruction is 32 bit wide and word aligned
What are the MicroBlaze bus interfaces?
  The MicroBlaze core has two bus interfaces:
    LMB: Local Memory Bus to access Only on-chip BRAMs
    OPB: IBM CoreConnect On-chip Peripheral Bus to access OPB compatible Peripherals

## Slide 17: Outline
MicroBlaze Core Architecture
MicroBlaze Core Configurations
Exceptions and Interrupts

## Slide 18: MicroBlaze Configurations
The MicroBlaze™ processor core is available in six configurations
These configurations differ in the bus interfaces the MicroBlaze core uses to interconnect to its peripherals
The configuration to use is design dependant and chosen by the user
The MicroBlaze configurations are:
  Configuration 1: IOPB+ILMB+DOPB+DLMB
  Configuration 2: IOPB+DOPB+DLMB
  Configuration 3: ILMB+DOPB+DLMB
  Configuration 4: IOPB+ILMB+DOPB
  Configuration 5: IOPB+DOPB
  Configuration 6: ILMB+DOPB

## Slide 19: MicroBlaze Configurations
Configuration 1: IOPB+ILMB+DOPB+DLMB
IOPB
DOPB
ILMB
DLMB
Dual Port Block Ram
OPB Memory Controller
OPB-to-OPB Bridge
OPB Interrupt Controller
OPB Timer/Counter
Data Side OPB
Data Side LMB
Instruction Side OPB
Instruction Side LMB
MicroBlaze Core
Notes: This diagram shows the architecture of a MicroBlaze system: MicroBlaze core and the peripherals on the CoreConnect bus. The MicroBlaze soft processor core is a standard RISC-based Harvard architecture that uses two separate buses: an instruction bus and a data bus. MicroBlaze soft processor uses the IBM CoreConnect peripheral interface bus. The peripherals used by MicroBlaze soft processor are the same peripherals that will be used with the PowerPC embedded on the Virtex-II PRO™ device. So all of the peripherals that connect to the MicroBlaze core also connect to Xilinx embedded PowerPC.
The CoreConnect bus architecture is licensed from IBM at no charge.
Use this configuration when your application requires more instruction and data memory than is available in the on-chip block RAM (BRAM). Critical sections of instruction and data memory can be allocated to the faster ILMB BRAM to improve your application’s performance.
Depending on how much data memory is required, the data-side memory controller may not be present. The data-side OPB is also used for other peripherals such as UARTs, timers, general purpose I/O, additional BRAM, and custom peripherals. The OPB-to-OPB bridge is required if the data-side OPB needs access to the instruction-side OPB peripherals, such as for software-based debugging, and also needed to put Application code into External Flash/RAM.

## Slide 20: MicroBlaze Configurations
Configuration 2: IOPB+DOPB+DLMB
IOPB
DOPB
DLMB
Block Ram
OPB Memory Controller
OPB-to-OPB Bridge
OPB Interrupt Controller
OPB Timer/Counter
Data Side OPB
Data Side LMB
Instruction Side OPB
MicroBlaze Core
Notes: Use this configuration when your application requires more instruction and data memory than is available in the on-chip BRAM. In this configuration, all of the instruction memory is resident in off chip memory or on-chip memory on the instruction-side OPB. Depending on how much data memory is required, the data-side memory controller may not be present. The data-side OPB is also used for other peripherals such as UARTs, timers, general purpose I/O, additional BRAM, and custom peripherals. The OPB-to-OPB bridge is only required if the data-side OPB needs access to the instruction-side OPB peripherals, such as for software-based debugging.

## Slide 21: MicroBlaze Configurations
Configuration 3: ILMB+DOPB+DLMB
DOPB
ILMB
DLMB
Dual Port Block Ram
OPB Interrupt Controller
OPB Timer/Counter
Data Side OPB
Data Side LMB
Instruction Side LMB
MicroBlaze Core
Notes: Use this configuration when your application code fits into the on-chip BRAM, but more memory may be required for data memory. Critical sections of data memory can be allocated to the faster DLMB BRAM to improve your application’s performance. Depending on how much data memory is required, the data-side memory controller may not be present. The data-side OPB is also used for other peripherals such as UARTs, timers, general purpose I/O, additional BRAM, and custom peripherals.

## Slide 22: MicroBlaze Configurations
Configuration 4: IOPB+ILMB+DOPB
IOPB
DOPB
ILMB
Dual Port Block Ram
OPB Memory Controller
OPB-to-OPB Bridge
OPB Interrupt Controller
BRAM Memory Controller
Data Side OPB
Instruction Side OPB
Instruction Side LMB
MicroBlaze Core
Notes: Use this configuration when your application requires more instruction and data memory than is available in the on-chip BRAM. Critical sections of instruction memory can be allocated to the faster ILMB BRAM to improve your application’s performance. The data side OPB is used for one or more external memory controllers and other peripherals such as UARTs, timers, general purpose I/O, additional BRAM, and custom peripherals. The OPB-to-OPB bridge is only required if the data-side OPB needs access to the instruction side OPB peripherals, such as for software-based debugging.

## Slide 23: MicroBlaze Configurations
Configuration 5: IOPB+DOPB
IOPB
DOPB
OPB Memory Controller
OPB-to-OPB Bridge
OPB Interrupt Controller
OPB Timer/Counter
Data Side OPB
Instruction Side OPB
MicroBlaze Core
Notes: Use this configuration when your application requires external instruction and data memory. In this configuration, all of the instruction and data memory is resident in off-chip memory or onchip memory on the OPB buses. The data-side OPB is used for one or more external memory controllers and other peripherals such as UARTs, timers, general purpose I/O, BRAM, and custom peripherals. The OPB-to-OPB bridge is only required if the data-side OPB needs access to the instruction-side OPB peripherals, such as for software based debugging.

## Slide 24: MicroBlaze Configurations
Configuration 6: ILMB+DOPB
DOPB
ILMB
Dual Port Block Ram
OPB Interrupt Controller
BRAM Memory Controller
Data Side OPB
Instruction Side LMB
MicroBlaze Core
Notes: Use this configuration when your application code fits into the on-chip ILMB BRAM, but more memory may be required for data memory. The data-side OPB is used for one or more external memory controllers and other peripherals such as UARTs, timers, general purpose I/O, additional BRAM, and custom peripherals.

## Slide 25: MicroBlaze Configurations
A MicroBlaze™ system = Processor core + OPB Ips
Some of the available OPB IP Peripherals:
  Timer/Counter Block
  Watchdog Timer/Timebase
  Interrupt Controller
  Flash/SRAM Controller
  SPI
  ZBT Memory Controller
  16550*/16450*/Lite UART
  IIC *
  Ethernet 10/100 MAC *
* Cost Option Peripherals
Notes: Please note that some OPB IP Peripherals are included with the MicroBlaze tools. Other OPB IP Peripherals are paid for peripherals, such as:
- 16550*/16450*/Lite UART
- IIC *
- Ethernet 10/100 MAC *
If the peripheral you require is not available, then you will need to create your own peripheral IP. This will require you to synthesize your component and interface it to the OBP.

## Slide 26: MicroBlaze Configurations
A MicroBlaze™ system is everything you want, nothing you don’t!
DOPB
ILMB
DLMB
Dual Port Block Ram
OPB UART Lite
OPB GPIO
Data Side OPB
Data Side LMB
Instruction Side LMB
MicroBlaze Core
Notes: The above example shows a possible implementation of the Configuration 3 of the MicroBlaze core. This simple example uses:
MicroBlaze core in Configuration 3
An OPB UART Lite
An OPB GPIO
A dual port block RAM hanging on the LMB Bus
This Particular Example, when implemented in Virtex-E 600 FPGA, uses only:
8 block RAMs: 11 % of the amount available in the Virtex-E 600 FPGA
622 Slices: 8 % of the slices resources in the Virtex-E 600 FPGA
The speed at which you can run the MicroBlaze soft processor depends upon several things: such as target device and the number and type of peripherals used. Using Dhrystone 2.1, the industry standard benchmark tool that exercises the integer-processing capabilities of a processor, we have found that the MicroBlaze soft processor provides 82 Dhrystone MIPS (D-MIPS) at 125MHz on a Virtex-II -5 target using UART and GPIO peripherals, and four block memories. Depending upon your MicroBlaze core configuration, your results may vary.

## Slide 27
Skills Check

## Slide 28: MicroBlaze Configurations Questions
What are the MicroBlaze™ bus interfaces?
Why would you need an OPB-to-OPB bridge, when you use both IOPB and DOPB sides?
What are the most common MicroBlaze configurations?

## Slide 29: MicroBlaze Configurations Answers
What are the MicroBlaze™ bus interfaces?
  MicroBlaze has two bus interfaces:
    LMB: Local Memory Bus to access only on-chip BRAMs
    OPB: IBM CoreConnect On-chip Peripheral Bus to access OPB compatible peripherals
Why would you need an OPB-to-OPB Bridge, when you use both IOPB and DOPB sides?
  The OPB-to-OPB bridge is only required if the data-side OPB needs access to the instruction-side OPB peripherals, such as for software-based debugging

## Slide 30: MicroBlaze Core Architecture Answers
What are the the most common MicroBlaze™ configurations?
  Configuration 1: IOPB+ILMB+DOPB+DLMB
  Configuration 3: ILMB+DOPB+DLMB

## Slide 31: Outline
MicroBlaze Core Architecture
MicroBlaze Core Configurations
Exceptions and Interrupts

## Slide 32: Exceptions & Interrupts
An Exception can be any condition that causes normal operation of the processor to be interrupted
An Exception could be caused by:
  An interrupt request from the hardware peripherals attached to the processor core
  A hardware reset
  A hardware break
  A software break
  An external interrupt request
Notes: An Exception can be any condition that causes normal operation to be interrupted, such as interrupts, (arithmetic overflow, and bus errors, not supported in the MicroBlaze core). In many RISC architectures there is a table of vectors that tells the processor where to jump for each of the possible conditions that could cause an exception. The hardware also handles the saving of state of the CPU and restoration of this state after the exception handler has completed.
The RISC philosophy, however, can be extended to the handling of exceptions. The processor also does not do any saving of the state information. The simplest implementation of an exception handler would be to mimic the the hardware in a RISC processor in software. In may applications there can be substantial performance gains by optimising the detection of the cause of the exception. As this is done purely in software, customised priority schemes can be developed, something that is often done to maximise the interrupt response.
When an exception occurs, the MicroBlaze soft processor stops the current execution to handle the exception. MicroBlaze soft processor branches to address 0x00000008 and uses the General Purpose Register 17 to store the address of the instruction that was to be executed when the exception occurred. The instruction located at the address where the current PC points to is not executed.

## Slide 33: MicroBlaze Interrupts Handling
A MicroBlaze™ core has Interrupt and Reset inputs
Currently the MicroBlaze soft processor has no software generated exception
Notes: When a Reset or a Debug_Rst occurs, MicroBlaze soft processor starts executing from address 0. PC and MSR are reset to the default values. When an Ext_Brk occurs, MicroBlaze soft processor starts executing from address 0x18 and stores the return address in register 16. An Ext_Brk is not executed if the BIP bit in MSR is active (equal to 1). When an Ext_NM_Brk occurs, MicroBlaze soft processor starts executing from address 0x18 and stores the return address in register 16. This occurs independent of the BIP bit value in MSR.
When an interrupt occurs, the MicroBlaze soft processor stops the current execution to handle the interrupt request. The Interrupt Latency is 4 Clock Cycles. MicroBlaze soft processor then branches to address 0x00000010 and uses the General Purpose Register 14 to store the address of the instruction that was to be executed when the interrupt occurred. It also disables future interrupts by clearing the Interrupt Enable flag in the Machine Status Register (setting bit 30 to 0 in MSR). The instruction located at the address where the current PC points to is not executed. Interrupts do not occur if the BIP bit in the MSR register is active (equal to 1).

## Slide 34: MicroBlaze Breaks
MicroBlaze™ soft processor has two kinds of breaks:
  Software (internal) breaks
  Hardware (external) breaks
Notes: Software Breaks
To perform a software break, use the brk and brki instructions. Refer to the Instruction Set Architecture documentation for more information on software breaks.
Hardware Breaks
Hardware breaks are performed by asserting the external break signal. When a hardware break occurs, the MicroBlaze soft processor core stops the current execution to handle the break. MicroBlaze soft processor branches to address 0x00000018 and uses the General Purpose Register 16 to store the address of the instruction that was to be executed when the break occurred. MicroBlaze soft processor also disables future breaks by setting the Break In Progress (BIP) flag in the Machine Status Register (setting bit 28 to 1 in MSR). The instruction located at the address where the current PC points to is not executed.
Hardware breaks are only handled when there is no break in progress (the Break In Progress flag is set to 0). The Break In Progress flag has higher precedence than the Interrupt Enabled flag. While no interrupts are handled when the Break In Progress flag is set, breaks that occur when interrupts are disabled are handled immediately. However, it is important to note that non maskable hardware breaks are always handled immediately.

## Slide 35: MicroBlaze Exceptions Table
Event
Exception
Reset
Debug_Rst
Interrupt
Ext_Brk
Ext_NM_Brk
Condition
Jump to
Return to
Null
0x00000008
Null
Null
MSR(30)=0
MSR(28)=0
Null
0x00000000
0x00000010
0x00000018
0x00000018
<R16>
<R16>
<R14>
NA
NA
<R17>
0x00000000
Notes: <Rx>: is the content of the Register Rx
NA: Non Applicable
The MSR: Machine Status Register
CC: Arithmetic Carry Copy Copy of the Arithmetic Carry (bit 29). Read only
BIP: Break in Progress (=0) No Break in Progress; (=1) Break in Progress. Source of break can be software break instruction or hardware break from Ext_Brk or Ext_NM_Brk pin.
C: Arithmetic Carry (=0) No Carry (Borrow); (=1) Carry (No Borrow)
IE: Interrupt Enable (=0) Interrupts disabled; (=1) Interrupts enabled
BE: Buslock Enable (=0) Buslock disabled on data-side OPB;
(=1) Buslock enabled on data-side OPB
Buslock Enable does not affect operation of ILMB, DLMB, or IOPB
0 28 29 30 31
CC BIP C IE BE

## Slide 36: Exceptions & Interrupts Questions
What is an Exception? And what may cause one?
What is the returning address of the MicroBlaze™ PC after:
  an Interrupt Service Routine?
  an Exception?
  a Reset?
  an External Break?

## Slide 37: Exceptions & Interrupts Answers
What is an Exception? And what may cause one?
  An Exception can be any condition that causes normal operation of the processor to be interrupted
  An Exception could be caused by:
    An Interrupt Request from the hardware peripherals attached to the processor core
    A hardware reset
    A hardware break
    A software break
    An External Interrupt Request

## Slide 38: Exceptions & Interrupts Answers
What is the returning address of the MicroBlaze™ PC after:
  an Interrupt Service Routine?
  <R14>
  an Exception?
  <R17>
  a Reset?
  0x00000000
  an External Break?
  <R16>

## Slide 39: Summary
The MicroBlaze™ soft processor core is a Harvard processor based on a RISC architecture
The MicroBlaze core processor is available in six configurations chosen according to the bus interfaces to the processor peripherals used
The MicroBlaze processor handles the Stack through Software and the user should think of the allocated stack size
The MicroBlaze soft processor ignores an erroneous instruction and does not generate any Exceptions while executing the instructions

## Slide 40: Appendix A: Instruction Set
Arithmetic Instructions
add Arithmetic Add
addi Arithmetic Add Immediate
mul Multiply
muli Multiply Immediate
rsub Arithmetic Reverse Subtract
rsubi Arithmetic Reverse Subtract Immediate
sext16 Sign Extend Halfword
sext8 Sign Extend Byte
Logical Instructions
and Logical AND
andi Logical AND with Immediate
andn Logical AND NOT
andni Logical AND NOT with Immediate
or Logical OR
ori Logical OR with Immediate
xor Logical Exclusive OR
xori Logical Exclusive OR with Immediate
Shift Instructions
sra Shift Right Arithmetic
src Shift Right with Carry
srl Shift Right Logical
bs Barrel Shift
bsi Barrel Shift Immediate
Load and Store Instructions
lbu Load Byte Unsigned
lbui Load Byte Unsigned Immediate
lhu Load Halfword Unsigned
lhui Load Halfword Unsigned Immediate
lw Load Word
lwi Load Word Immediate
sb Store Byte
sbi Store Byte Immediate
sh Store Halfword
shi Store Halfword Immediate
sw Store Word
swi Store Word Immediate
Branch Instructions
beq Branch if Equal
beqi Branch Immediate if Equal
bge Branch if Greater or Equal
bgei Branch Immediate if Greater or Equal
bgt Branch if Greater Than
bgti Branch Immediate if Greater Than
ble Branch if Less or Equal
blei Branch Immediate if Less or Equal
blt Branch if Less Than
blti Branch Immediate if Less Than
bne Branch if Not Equal
bnei Branch Immediate if Not Equal
br Unconditional Branch
bri Unconditional Branch Immediate
Special Instructions
brk Break
brki Break Immediate
imm Immediate
mfs Move From Special Purpose Register
mts Move To Special Purpose Register
rtid Return from Interrupt
rtsd Return from Subroutine