## Slide 1: User-Defined Peripherals

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the reason for user-defined peripherals
Describe the search algorithm for user-defined peripherals
Specify a peripheral using the SIF format
State the effects of attributes
Describe the peripheral common libraries
Specify the black box peripheral flow

## Slide 3: Outline
Reasoning
Building a Custom Peripheral
Interfacing with EDK
Summary

## Slide 4: Why Custom Peripherals?
EDK is supplied with many peripherals
  Memory controllers
  Interrupt controllers
  UART / JTAG
  GPIO
There are always going to be requirements for custom peripherals
  Military bus interface
  My-protocol v2.0 interface
Notes: There is often going to be the case where a user system cannot only contain peripherals that are included in the EDK. Custom peripherals are required to interface to standards that are not supported by the MicroBlaze™ soft processor, and also peripherals that are non-standard or not popular may not be included with the kit.
This module shall introduce the methods for including custom peripherals into a MicroBlaze system.

## Slide 5: Why Custom Peripherals?
There are many ways to connect up to a custom interface:
1. Connect it to some GPIO
O
P
B
GPIO
Interface Logic
MicroBlaze
DAC
Notes: In order to connect up a custom interface, you can use some of the peripherals that are already available within EDK.
This example shows the use of the GPIO peripheral to create Memory-Mapped registers that can be written to and also read from.
If the custom interface needs to connect to just one address on the bus, the GPIO is an effective method of interfacing.

## Slide 6: Why Custom Peripherals?
There are many ways to connect up to a custom interface:
2. Interface to an OPB block RAM
O
P
B
BRAM
Interface Logic
MicroBlaze
Memory - Mapped VGA Palette
Notes: GPIO is good for a small number of signals. However, often, an interface might require a region of memory in order to communicate effectively to the system.
If the region of memory is of a suitable size, then this could be stored within block RAM components within the Xilinx FPGA.
The OPB block RAM peripheral is a dual-port block RAM. The second (B) port of the block RAM is not connected to the OPB bus and is available for user connection.
This can be an effective manner for connecting up to custom interfaces if the memory space used by the device is small.

## Slide 7: Why Custom Peripherals?
There are many ways to connect up to a custom interface:
3. Convert the bus to look like RAM / ROM
O
P
B
EMC
MicroBlaze
Notes: Sometimes the custom interface is in the form of a separate bus, and so a bridge needs to be constructed to interface to these.
One method of connecting several buses together would be to generate some logic to make the interface look like a RAM device. In this way, you could interface to the External Memory controller for access to devices on this bus.

## Slide 8: Why Custom Peripherals?
Connecting directly to the OPB has many advantages:
  Less latency
    No intermediate peripherals blocking the data path
  Direct memory mapping
    The peripheral appears as memory to the system
  Smaller
    GPIO / EMC controllers add size with functionality.
    Block RAMs are limited in size and use up resources
  Specific
    The user has direct control over functionality and implementation
Notes: The previous solutions are all valid and should work for the situations mentioned.
However, with the addition of intermediate peripherals, you could be increasing the size and latency of the design.
You can interface directly to the OPB and create your own peripheral. This peripheral shall be specific to the function that is required and so should be more optimal as a solution.

## Slide 9: Outline
Reasoning
Building a Custom Peripheral
Interfacing with EDK
Summary

## Slide 10: Building a Custom Peripheral
All peripherals need to connect to the OPB bus, either as a slave or a master peripheral
Notes: All peripherals need to connect to a bus in order to carry out their function.
The On-Chip Peripheral Bus has been developed by IBM for the purpose of connecting peripherals. The specification for this bus can be found on the IBM website.
At time of publishing, this was available at
http://www-3.ibm.com/chips/products/coreconnect/
The bus structure is described in detail in the MicroBlaze Buses module. However, at a simple level, it can be described as an or-gate structured bus with control signals and support for multiple masters and multiple slave peripherals.

## Slide 11: Building a Custom Peripheral
OPB slaves can have latency from 1 to 16 OPB clock cycles
If the latency is more than 16 clock cycles, “Sln_toutSup” needs to be asserted to prevent the arbiter from releasing the bus
Sln_xferAck is asserted by the slave for one clock cycle to indicate the end of a successful bus transaction
Microprocessor write transaction
  Data bus read and Xfer_Ack is asserted
Microprocessor read transaction
  Data bus is valid on the peripheral output data bus during assertion of Xfer_Ack
Notes: The OPB has the possibility to deal with peripherals of variable latency. The latency of a peripheral can be from 1 to 16 clock cycles.
If a peripheral requires latency on the bus of more than 16 clock cycles (this would severely impact on performance), a signal 'ToutSup' can be asserted. This disables the arbiter from declaring a peripheral timeout.
Read and write transactions are described in detail in the Buses module. However, Xfer_Ack is a particularly important signal.
This signal is to acknowledge the data transfer and is asserted by the peripheral. In a write transaction, the Microprocessor must keep the data valid on the bus until the Xfer_ACK signal is asserted. On a read operation, the peripheral must be outputting valid data during the assertion of the Xfer_ACK signal.

## Slide 12: OPB Slave Interaction
A slave should respond to a transaction
  In its address range
  When OPB_select is asserted
A slave should get off the bus when
  OPB_select is released
  The transaction has finished
When not on the bus, a slave should set its data output to 0
OPB_select
M1_select
M1_rnw
M1_Abus
SI2_xferack
SI2_DBus
SI2_DBusEn
Valid Address
Valid Data
The Slave specifies the end of the transaction
The transaction takes place
Notes: The OPB_select signal can be thought of as an enable for the rest of the bus circuitry. If the OPB_select signal is not asserted, then the address, and data busses are not valid. The peripheral should not assert any bus signals when OPB_Select is low.

## Slide 13: Sample PB Decoding Logic
Notes: The above illustration is an example of a possible implementation of address decoding and the logic that makes up the Xfer_ACK signal.
It should be noted that for clarity, only 8 address bits are shown in this diagram. MicroBlaze™ is a 32-bit Microprocessor and so has 32 address lines. The number of address bits to decode is dependent on the address range of the peripheral.

## Slide 14: Sample Address Decoding Logic
Address decoding is simple - Invert and AND the OPB Address bus as required for the peripheral address
Then enable the output when opb_select is valid (high)
Wide AND Structure
Notes: Address decoding is simply a comparator. This can be implemented in the Xilinx logic as a wide input AND gate. Additionally, OPB_SEL must be asserted in order to enable the address decoding logic.
This address decoding can be treated as a chipselect for the peripheral.

## Slide 15: Sample Address Decoding Logic
The address bus can be a critical timing path
Xilinx has created an optimal component for this - pselect.vhd
  Uses fast carry logic to minimize delay
Notes: The address decoding on the previous slide was a wide AND-gate. This is combinatorial logic and can therefore severely affect the performance of the system.
To minimize this, a library element, Pselect, has been created. This uses fast carry logic in order to implement this address decoder as efficiently as possible.

## Slide 16: Sample Address Decoding Logic
Pselect.vhd is in the EDK common libraries
Instantiate pselect into your peripheral for optimal address decoding
entity pselect is
generic (
C_AB : integer := 9;
C_AW : integer := 32;
C_BAR : std_logic_vector(0 to 31) := X"33000000"
);
port (
A : in std_logic_vector(0 to C_AW-1);
AValid : in std_logic;
PS : out std_logic
);
end entity pselect;
Number of MS Bits to address decode (Dictates peripherals address range)
Base Address to decode
OPB Address Bus
Peripheral Select
Notes: Pselect is available in the EDK common libraries and the generic and port declarations are shown above.
Note that this component is completely generic, including the address to be decoded.
In this way, a peripheral can be generic, passing the address attributes down to the address decoder. This would allow the address ranges for the various peripherals to be set at runtime with the mhs file, rather than being hard-coded in the logic.

## Slide 17: Sample Xfer_ACK Signaling
Xferack must only be asserted for one clock cycle
  The above flip flop ‘memory’ ensures this
Xferack is cancelled with opb_rst
Peripheral Select Signal from Address Decoding
Notes: Xfer_ACK is an important signal both for peripheral reading and writing. The above schematic illustrates a simple way to deal with this signal. Note that this logic creates the XferACK signal after one clock cycle. If a different latency is required then this would need to be modified.
The OPB_Rst signal is to reset the bus. This is connected to the reset signals on the flip flops to perform this function.
The circuit generates a high output on Xfer_ACK one cycle after the peripheral select signal goes high. The and-gate and register then dissasert the signal after the initial clock cycle.
Xfer_ack then cannot be reasserted until the peripheral address select signal is disasserted (at the end of the bus transaction)

## Slide 18: Outline
Reasoning
Building a custom peripheral
Interfacing with EDK
Summary

## Slide 19: Interfacing with EDK – SIF Structure
Custom Peripherals need a specific file structure
  Standard Interface Format (SIF)
The custom peripheral directory is split into software (\drivers), and hardware (\myip)
The full SIF specification is available in the Embedded System Tools Guide
Notes: For the EDK tools to use custom peripherals, the SIF file structure is required. By using the SIF structure, the peripheral hardware and software are organised in a way that the tools expect, and the configuration files (.mpd, .pao, .bbd, .mdd) are available for the tools to query.

## Slide 20: Interfacing with EDK-.mpd
Every EDK peripheral has a .mpd (Microprocessor Peripheral Definition) file
The .mpd file contains:
  Version control and peripheral naming
  Port information
  Attributes
  Default values
The file is ASCII and very simple to write
Notes: The Microprocessor Peripheral definition file is described in detail in the Peripherals module. It contains all the information that is required in order to connect the peripheral to a Microprocessor system.

## Slide 21: Interfacing with EDK-.mpd
VHDL generics
Corresponding .mpd file parameters
entity opb_7seg is
generic (
C_OPB_AWIDTH : integer := 32;
C_OPB_DWIDTH : integer := 32;
C_BASEADDR : std_logic_vector := X"2000_0000";
C_HIGHADDR : std_logic_vector := X"2000_00FF";
C_NUM_LED : integer := 9
);
PARAMETER C_OPB_DWIDTH = 32, DT=integer
PARAMETER C_OPB_AWIDTH = 32, DT=integer
PARAMETER C_BASEADDR = 0x20000000, DT=std_logic_vector, BUS=SOPB, MIN_SIZE=0
PARAMETER C_HIGHADDR = 0x200000FF, DT=std_logic_vector, BUS=SOPB
PARAMETER C_NUM_LED = 9, DT=integer
PARAMETER VERSION = 2.0.0
BEGIN opb_7seg, IPTYPE=PERIPHERAL, HDL=VHDL
# Define bus interface
BUS_INTERFACE BUS=SOPB, BUS_STD=OPB, BUS_TYPE=SLAVE
.mpd file header
Notes: It can be seen that after the header, the VHDL and .mpd files are very similar.
This slide shows the correspondence between the generic settings in the VHDL to the parameters in the .mpd

## Slide 22: Interfacing with EDK-.mpd
Example VHDL Port
Corresponding Example .mpd port declaration
port (
OPB_Clk : in std_logic;
OPB_Rst : in std_logic;
-- OPB signals
OPB_ABus : in std_logic_vector(0 to C_OPB_AWIDTH-1);
OPB_BE : in std_logic_vector(0 to C_OPB_DWIDTH/8-1);
OPB_DBus : in std_logic_vector(0 to C_OPB_DWIDTH-1);
OPB_RNW : in std_logic;
OPB_select : in std_logic;
OPB_seqAddr : in std_logic;
GPIO_DBus : out std_logic_vector(0 to C_OPB_DWIDTH-1);
GPIO_errAck : out std_logic;
GPIO_retry : out std_logic;
GPIO_toutSup : out std_logic;
GPIO_xferAck : out std_logic;
-- LED signals
LED_A : out std_logic_vector(C_NUM_LED downto 0);
LED_B : out std_logic_vector(C_NUM_LED downto 0);
LED_C : out std_logic_vector(C_NUM_LED downto 0);
LED_D : out std_logic_vector(C_NUM_LED downto 0);
LED_E : out std_logic_vector(C_NUM_LED downto 0);
LED_F : out std_logic_vector(C_NUM_LED downto 0);
LED_G : out std_logic_vector(C_NUM_LED downto 0)
);
PORT OPB_Clk = "", DIR=IN, BUS=SOPB, SIGIS=CLK
PORT OPB_Rst = OPB_Rst, DIR=IN, BUS=SOPB
PORT OPB_ABus = OPB_ABus, DIR=IN, VEC=[0:C_OPB_AWIDTH-1], BUS=SOPB
PORT OPB_BE = OPB_BE, DIR=IN, VEC=[0:C_OPB_DWIDTH/8-1], BUS=SOPB
PORT OPB_DBus = OPB_DBus, DIR=IN, VEC=[0:C_OPB_DWIDTH-1], BUS=SOPB
PORT OPB_RNW = OPB_RNW, DIR=IN, BUS=SOPB
PORT OPB_select = OPB_select, DIR=IN, BUS=SOPB
PORT OPB_seqAddr = OPB_seqAddr, DIR=IN, BUS=SOPB
PORT GPIO_DBus = Sl_DBus, DIR=OUT, VEC=[0:C_OPB_DWIDTH-1], BUS=SOPB
PORT GPIO_errAck = Sl_errAck, DIR=OUT, BUS=SOPB
PORT GPIO_retry = Sl_retry, DIR=OUT, BUS=SOPB
PORT GPIO_toutSup = Sl_toutSup, DIR=OUT, BUS=SOPB
PORT GPIO_xferAck = Sl_xferAck, DIR=OUT, BUS=SOPB
PORT LED_A = LED_A, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
PORT LED_B = LED_B, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
PORT LED_C = LED_C, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
PORT LED_D = LED_D, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
PORT LED_E = LED_E, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
PORT LED_F = LED_F, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
PORT LED_G = LED_G, DIR=OUT, VEC=[C_NUM_LED:0], ENDIAN=LITTLE
Notes: The port settings are also mapable line-by line and follow a similar format.

## Slide 23: Interfacing with EDK-.pao
Custom peripherals often consist of multiple HDL files
With VHDL, synthesis is sensitive to analysis order
  The PAO file specified the Peripheral Analysis Order
.pao file
Notes: When synthesizing any VHDL, the synthesis order is important.
In order for the Platform Generator to synthesize the peripheral correctly, a Peripheral Analyze Order file is specified.

## Slide 24: Interfacing with EDK-.pao
Example .pao file for this peripheral
lib common_v1_00_a common_types_pkg
lib common_v1_00_a pselect
lib opb_7seg_v2_00_a gpio_core
lib opb_7seg_v2_00_a hex_to_7seg
lib opb_7seg_v2_00_a opb_7seg
Synthesis analyse order
Pselect.vhd (Part of the common libraries - common_v1_00_a)
Gpio_core.vhd
Opb_7seg.vhd
Hex_to_7seg.vhd
My OPB  7 Segment Custom Peripheral
Notes: This example shows that the top level (opb_7seg.vhd) is synthesized last, after all of the dependencies are analyzed.

## Slide 25: Interfacing with EDK-.bbd
Some peripherals include black box components
  E.g., peripherals that contain COREGen modules
  Peripherals that contain protected IP
  Hand-crafted netlists
These netlists are included into a design, using a Black Box Description (.bbd) file
More information on the .bbd file can be found in the MicroBlaze™ Peripheral module
.bbd file
Notes: The Black Box Definition file is a lookup table for netlists to be included in the implementation project. More information about this format is in the peripherals presentation.

## Slide 26: Interfacing with EDK- Drivers
Software drivers are often included with a peripheral
MDD file specifies driver levels and which files to use
BEGIN driver XOPB7seg
constant VERSION = 2.0.0
parameter LEVEL = 0
END
BEGIN level 0
constant copyfiles = ALL
END
.mdd file
Notes: The MDD file specified the drivers to use within the system. The driver levels (0,1,2) are specified by the user, and the header files are copied to the includes directory of the project as required.

## Slide 27: Interfacing with EDK - Drivers
The Makefile specifies how the code is compiled, the library it is compiled into, and where files are copied
Makefile, c files and header files
COMPILER=mb-gcc
ARCHIVER=mb-ar
CP=cp
COMPILER_FLAGS=-O2 -c
EXTRA_COMPILER_FLAGS=
LIB=libc.a
LEVEL=0
RELEASEDIR=../../../lib
INCLUDEDIR=../../../include
INCLUDES=-I./. -I${INCLUDEDIR}
L0_INCLUDEFILES=7seg.h
L1_INCLUDEFILES=7seg.h
LIBSOURCES=*.c
INCLUDEFILES=$(L$(LEVEL)_INCLUDEFILES)
OUTS = *.o
libs: L$(LEVEL)_LIBS
L0_LIBS:
echo "Compiling 7 Segment Custom Peripheral Level 0"
$(COMPILER) $(COMPILER_FLAGS) $(EXTRA_COMPILER_FLAGS) $(INCLUDES) $(LIBSOURCES)
$(ARCHIVER) -r ${RELEASEDIR}/${LIB} $(OUTS)
make clean
L1_LIBS:
echo "Compiling 7 Segment Custom Peripheral Level 1"
$(COMPILER) $(COMPILER_FLAGS) $(EXTRA_COMPILER_FLAGS) $(INCLUDES) $(LIBSOURCES)
$(ARCHIVER) -r ${RELEASEDIR}/${LIB} $(OUTS)
make clean
include:
${CP} $(INCLUDEFILES) $(INCLUDEDIR)
clean:
rm -rf ${OUTS}
Notes: In addition to an MDD file, each source directory for drivers has a makefile. This makefile is run by libgen in order to compile the required libraries.
It is useful to have an ECHO command within the compilation so you have an indication that the correct drivers are compiled when you runs Libgen.

## Slide 28: Interfacing with EDK - Gotchas
Make sure that your peripheral is fully functioning and working as expected before running software on it
  Software debug is not intended to test out hardware
  Use HDL simulation to debug buggy peripherals
  The CoreConnect toolkit can also help out with debugging cores
Make sure that you add the Custom Peripheral repository path to Libgen and Platgen (-P)
Ensure that the custom peripheral drivers are compiled into the correct library, and use mb-objdump to ensure the drivers really are there

## Slide 29: Outline
Reasoning
Building a custom peripheral
Interfacing with EDK
Summary

## Slide 30: Review Questions
What logical structure forms the OPB bus?
Which signal should be used as the input qualifier for address decoding logic?
Which OPB common library assists with fast carry-logic address decoding?
Without assertion of any timeout signals, after how many cycles should a slave get off the bus?
For how long should the Xfer_ACK signal be asserted on completion of a data transfer?
Which of the following is required for all peripherals? .pao .bbd .mhs .mpd .mdd .mvs

## Slide 31: Answers
What logical structure forms the OPB bus?
  The OPB bus consists of an OR gate structure for combining data lines, and an OR gate structure for combining address lines
Which signal should be used as the input qualifier for address decoding logic?
  The OPB_sel line is the qualifier for a valid OPB bus operation
Which OPB common library assists with fast carry-logic address decoding?
  The Peripheral Select (pselect.vhd) library component provides a generic approach to fast carry-logic-based address decoding

## Slide 32: Answers
Without assertion of any timeout signals, after how many cycles should a slave get off the bus?
  The OPB specification requires a data transfer to be complete within 16 OPB Clock cycles. If the TOUT_SUP signal is not asserted within this time, the arbiter shall kick the slave off of the bus
For how long should the Xfer_ACK signal be asserted on completion of a data transfer?
  Xfer_ACK is required to be asserted for one clock cycle
Which of the following is required for all peripherals? .pao .bbd .mhs .mpd .mdd .mvs
  Every peripheral has to have a Microprocessor Peripheral Definition (.mpd) file. Other files may be used, depending on the configuration and functionality of the peripheral

## Slide 33: Summary
OPB Peripherals are not difficult to write!
The peripheral should take no longer than 16 OPB clock cycles, or extra logic is required to communicate to the arbiter
Pselect.vhd in the common library is the fastest way to implement address decoding
Xfer_ACK should be signaled on a master write to indicate success and on a Master read to indicate valid data on the bus
OPB_sel indicates that the bus signals are valid