## Slide 1: Libgen
The Library Generator

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the function of the Library Generator
Understand the MSS structure and the different attributes
Use the Library Generator

## Slide 3: Outline
Introduction
MSS Structure & Parameters
Using Libgen
Xilinx Libraries
Summary

## Slide 4: What is Libgen
Software utility provided for Platform’s Firmware Development
Libgen configures libraries and device drivers
The MSS (Microprocessor Software Specification) file defines the:
  Standard input/output devices
  Interrupt handler routines
  and other related software features (file system, etc.)
Libgen configures libraries and drivers with the information in the MSS input file
Notes: MSS: Microprocessor Software Specification
The Library Generator (libgen) is generally the first tool to run to configure libraries and device drivers. An MSS file is created by the user (or by XPS if instructed to do so) and given to libgen as input. The MSS file defines the standard input/output devices, interrupt handler routines, and other related software features.
Libgen configures libraries and drivers with the information in the MSS input file.

## Slide 5: Libgen Input/Output Files
Libgen takes the MSS file as input
Libgen generates the following files:
  xmdstub.elf
  bootstrap.elf
Libgen generates the following directories:
  Include
  Lib
  libsrc
Notes: Libgen generates these directories and files in the MICROBLAZE_PROJECT directory:
include
The include directory contains C header files that are needed by drivers. These files define base addresses of the peripherals in the system and also define function prototypes.
lib
The lib directory contains libc.a and libm.a libraries. More information on the libraries can be found in the Libraries documentation.
libsrc
The libsrc directory contains intermediate files and makefiles that are needed to compile the libraries and drivers. The directory contains peripheral specific driver files that are copied from the MicroBlaze soft processor and user driver directories. Please refer to the Drivers subsection of this document for more information. Note that this directory is overwritten each time libgen is run.
Code
The code directory may be used as a repository for MicroBlaze executables, xmdstub.elf, and bootstrap.elf, as well as the system source code.

## Slide 6: Outline
Introduction
MSS Structure & Parameters
Using Libgen
Xilinx Libraries
Summary

## Slide 7: What is an MSS File
The MSS: Microprocessor Software Specification file
Is the heart of the processor system for software development
Assigns software drivers to each peripheral in the system
Assigns interrupt software functions to peripherals
Assigns different software .elf files to different processor modes:
  Debug: xmdstub.elf
  Bootstrap: bootsrap.elf
Allocates which peripherals are mapped as STDIN & STDOUT devices
Assigns which peripheral instance is used as debug peripheral in the system
Assigns which peripheral instance is used as boot peripheral for the MicroBlaze processor

## Slide 8: What is an MSS File
‘C’ File
“Print”
STD_IO
MSS File
UART
“Outbyte”
Driver
UART
“Inbyte”
Driver
MHS File
0xFFFFFFFF
0x00000000
4 GigB
My_Microblaze Local Memory
myuart UART
0x00001FFF
0xFFFF0200
0xFFFF02FF
Notes: As can be seen from the above diagram, the MSS file contains the information required to bring together the hardware and the software. In this example, the standard IO Stream (for printing, and reading inputs) are both specified to be for a UART. This UART is then cross-referenced with the MHS file, to find its address, and the drivers are compiled into the library according to the UART’s characteristics, and address.

## Slide 9: MSS File Example
PARAMETER VERSION = 2.0.0
PARAMETER HW_SPEC_FILE = system.mhs
BEGIN PROCESSOR
PARAMETER HW_INSTANCE = My_MicroBlaze
PARAMETER DRIVER_NAME = cpu
PARAMETER DRIVER_VER = 1.00.a
PARAMETER EXECUTABLE = My_MicroBlaze/code/system.elf
PARAMETER COMPILER = mb-gcc
PARAMETER ARCHIVER = mb-ar
PARAMETER DEFAULT_INIT = XMDSTUB
PARAMETER SHIFTER = FALSE
PARAMETER DEBUG_PERIPHERAL = myjtaguart
PARAMETER BOOT_PERIPHERAL = myjtaguart
PARAMETER STDIN = myuart
PARAMETER STDOUT = myuart
END
Global Parameters: System Specific
Processor Instance Specific Parameters
Notes: The MSS file example above, and on the next slide, are defining a simple MicroBlaze System including:
+ UARTLite: instance myuart
+ JTAGUART: instance myjtaguart
+ GPIO: instance mygpio
+MicroBlaze Core: instance Mymicroblaze.
This MSS file has three main sections:
1- Global Parameters specification section at the head of the file:
+ PSF Version = 2.00.0
+ MHS file = system.mhs (in the same directory as the MSS file)
2- Followed by the Processor Instance Section:
where different Parameters related to the Processor Instance are specified.
3- And the following Section is for Drivers Specification parameter for each Instance of OPB IP Peripheral included in the MicroBlaze:
+ LMB Controller section
+ UARTLite section
+ GPIO section
+ JTAGUART section

## Slide 10: MSS File Example
BEGIN DRIVER
PARAMETER HW_INSTANCE = mylmblmb_cntlr
END
BEGIN DRIVER
PARAMETER HW_INSTANCE = myuart
PARAMETER DRIVER_NAME = uartlite
PARAMETER DRIVER_VER = 1.00.b
END
BEGIN DRIVER
PARAMETER HW_INSTANCE = mygpio
PARAMETER DRIVER_NAME = gpio
PARAMETER DRIVER_VER = 1.00.a
PARAMETER LEVEL = 1
END
BEGIN DRIVER
PARAMETER HW_INSTANCE = mjtaguart
PARAMETER DRIVER_NAME = uartlite
PARAMETER DRIVER_VER = 1.00.b
PARAMETER LEVEL = 0
END
Drivers Specification for myuart instance
Drivers Specification for mygpio instance
Drivers Specification for myjtaguart instance
LMB Controller Specific Parameters: No Drivers Specified for this Instance
Notes: Each Drivers Specification section:
+ Starts by the keyword BEGIN DRIVER
+ Closed by the END keyword
+ Specifies the IP Instance name by the PARAMETER HW_INSTANCE
+ Specify the Driver name: DRIVER_NAME, as specified in the EDK Install directory, or if it is a Custom Driver, as named by the User.
+ Specify the Driver version, DRIVER_VER = 1.00.a
+ Specify the LEVEL of Drivers used (0, 1, or 2)

## Slide 11: File System & Interrupt
BEGIN FILESYS
parameter FILESYS_NAME = XilMfs
parameter PROC_INSTANCE = My_Microblaze
parameter MOUNT = "/dev/mfs"
parameter LIBRARY = XilFile
END
BEGIN DRIVER
parameter HW_INSTANCE = my_jtag
parameter DRIVER_NAME = uartlite
parameter DRIVER_VER = 1.00.a
parameter INT_HANDLER = jtag_uart_handler, INT_PORT = Interrupt
END
File System
Interrupt Service Routine Specification
Notes: The users can write application to either interact directly with the underlying file systems and devices or make use of the LibXil File module to integrate with file systems and devices. The Libgen attribute LIBRARY indicates that LibXil File module should be compiled into the project specific Libraries. To use Memory File System with LibXil File component, use the following code in the MSS File.
The parameter LIBRARY = XilFile is needed to access a device through Xilfile.
All devices that have stream based input/output mechanism are supported through LibXil File.
The second section is an MSS entry for a my_jtag instance of a JTAGUART OPB IP Peripheral. Note that the JTAGUART uses the UART Lite drivers and it does specify the ISS (Interrupt Service Routine): jtag_uart_handler.c that gets called when the JTAGUART raises an Interrupt.

## Slide 12: MSS File Parameters
Option
Description
STDIN
STDOUT
BOOT_PERIPHERAL
DEBUG_PERIPHERAL
This specifies that the peripheral is the standard input
This specifies that the peripheral is the standard output
This attribute specifies the peripheral in the MHS file to be the debug
peripheral. This peripheral will be used for on board debug purposes
This attribute specifies the peripheral in the MHS file to be the boot
peripheral. This peripheral will be used for bootstrap purposes
VERSION
This is the PSF (Standard Interface Format) version parameter, needs to be specified in the global parameters section.
HW_SPEC_FILE
This parameter points to the MHS file (Microprocessor Hardware Specification)
EXECUTABLE
This parameter specifies the location of the executable file for a given Processor Instance
COMPILER
This parameter specifies the compiler used to generate the elf files for the Processor Instance (mb-gcc) by default
Notes: STDIN & STDOUT:
Peripherals that handle I/O need drivers to access data. Two files, inbyte.c, outbyte.c are required in the driver directory if the peripheral instance can be both standard input and standard output. The peripheral instance should be specified as STDIN or STDOUT in the MSS file.
Boot and Debug Peripherals:
These are peripherals that are specifically used to download bootstub and xmdstub. The Parameters BOOT_PERIPHERAL and DEBUG_PERIPHERAL are used for denoting the boot and debug peripheral instances. Libgen uses these attributes in xmdstub and bootstrap modes.
Drivers:
Most peripherals require software drivers. The EDK peripherals are shipped with associated drivers. Refer to the Libraries and Device Drivers documentation for more information. The DRIVER parameters must be used in the MSS file to specify the drivers’ characteristics for a peripheral.
There is no default value for this attribute. The driver directory contains C source and header files and a makefile for the driver.

## Slide 13: MSS File Parameters
Option
Description
MOUNT
LIBRARY
DRIVER_VER
DRIVER_NAME
INT_HANDLER
This parameter specifies the mount name of a file system
This parameter specifies that the file or device is accessed using Xilinx libraries
This parameter defines the interrupt handler function for a peripheral’s interrupt signalV
This parameter specifies the name of the driver directory to be used for the peripheral requiring a driver
This parameter specifies the driver version to be used
HW_INSTANCE
This parameter specify the instance name given to the peripheral in the MHS file for a given OPB IP peripheral
LEVEL
This parameter specifies which level of driver is required for the firmware application (Level 0, 1 or 2)
DEFAULT_INIT
This parameter defines the default C Run Time routine to be used
ARCHIVER
This parameter specifies the tools used to archive Object files into a Library, (mb-ar) by default
Notes: Libgen copies this directory over to the $MICROBLAZE_PRJ/libsrc directory and runs make for compiling the driver. Refer to the source codes and makefiles in the drivers directory for more information. Libgen also creates an include file xparameters.h in the $MICROBLAZE_PRJ/include directory. This header file must be included in the driver source files. This file contains peripheral base address definitions and interrupt masks for the peripherals. This file also contains function prototypes and useful defines. You can write their own drivers. These drivers must be in a specific directory under $MICROBLAZE_PRJ/drivers or $XIL_MYPERIPHERALS/drivers. The DRIVER attributes allow you to specify any name for their drivers.
Interrupts & interrupt Controller:
An interrupt controller peripheral must be instantiated if the MHS file has multiple interrupt signals defined. The MHS file should also have a PRIORITY attribute associated with each interrupt signal. In the MSS file, the INT_HANDLER attribute allows an interrupt handler routine to be associated with the interrupt signal. Libgen uses this attribute to configure the interrupt controller handler to call the appropriate peripheral handlers on an interrupt. The functionality of these handler routines is left to you to implement. If INT_HANDLER attribute is not specified, libgen uses a default dummy handler routine for the peripheral. If there is only one interrupt driven peripheral, an interrupt controller need not be used. However, the peripheral should still have an interrupt handler routine specified. Otherwise a default one is used.

## Slide 14: Outline
Introduction
MSS Structure & Parameters
Using Libgen
Xilinx Libraries
Summary

## Slide 15: Using Libgen

## Slide 16: Library Generation - Libgen
Must be run before the C can be compiled
Gets the required drivers – (subroutines for input / output)
Puts the drivers in the ./include directory
Configures the drivers for the required address locations – E.g., the UART is at address 0xFFFF8000
Customizes library header files for your system

## Slide 17: Running Libgen
libgen <options> <filename.mss>
mss input file
Notes: This is a template for calling the library generator.
The architecture is important to the library generator, as the architecture of the MicroBlaze changes depending on this. The Virtex-II has embedded multipliers, which are used by the processor. However, this is not the case for the Virtex architectures.
The Mode specifies how we want our system to behave.
Executable mode would use the compiled C code to execute as expected in the C code. The libraries would be generated accordingly
XMDStub is a special debug mode. Instead of the users C code being loaded into the system, a debugging ‘stub’ would be used, and source code for this would be linked to the debug peripheral defined in the MSS file.
Bootstrap mode is another special mode. The code for this is pre-defined, as with the XMD Stub mode, and would be linked to the peripheral. In this mode, you could boot up the MicroBlaze soft processor core to accept instruction input from a UART connected to a PC.

## Slide 18: Running Libgen
Calling Libgen from XPS

## Slide 19: Libgen Options
Option
Description
-h, -help
-p, -proj
-a, -arch
-v, -ver
-m, -mode
-P, -Per_Dir
This option displays the usage menu and quits
This option displays the version number of libgen
This option defines the target architecture family. The options are Spartan-II, Spartan-IIE, Virtex, Virtex E or Virtex-II
This option specifies the project directory. The default is the current directory
This option specifies the user peripherals and drivers directory. Libgen looks for drivers in the directory <PER_DIR>/drivers/
This option is Global, allows libgen to be run in one of the following modes: executable (default mode), xmdstub, or bootstrap
-d, -do_not_warn
This option disables printing of warning messages. By default, all warnings are printed

## Slide 20: Libgen Options
Option
Description
-x, -xmdstub
-e, -executable
-s, -stub
-l, -lib
This option is specific to a Processor Instance in the system: Specifies that one or more processors have their memory initialized with xmdstubs (debug stubs)
This option can be used to copy libraries and drivers but not compile them
Creates the stub files (for MicroBlaze) and BRAM initialization script. Using this option prevents the generation of libraries and drivers
-b, -bootstub
Same as the -x Option for the Bootstub Mode
Same as the -x Option for the Executable Mode
Notes: -x, -xmdstub proc_inst_name_1 [, proc_inst_name_2, ...]
Specifies that one or more processors have their memory initialized with xmdstubs (debug stubs). Whereas the -mode option is a global option applicable for all processors in the system, this option can be used to specify initialization modes for specific processor instances. When both -mode and xmdstub options are used, the -xmdstub option takes precedence for that processor instance alone.
-b, -bootstub proc_inst_name_1 [, proc_inst_name 2, ...]
-e, -executable proc_inst_name_1 [, proc_inst_name_2, ...]
-s, -stub
Creates the stub files (for MicroBlaze) and BRAM initialization script run_download.sh (solaris) or run_download.bat (windows) only. Using this option prevents the generation of libraries and drivers.

## Slide 21: Outline
Introduction
MSS Structure & Parameters
Using Libgen
Xilinx Libraries
Summary

## Slide 22: Xilinx Libraries
The EDK provides three libraries:
Math library (libm)
Standard C language support (libc)
Xilinx drivers and libraries (libxil)
Notes: Most of the routines in the library are written in C and can be ported to any platform.
The Library Generator (Libgen) configures the libraries for an embedded processor using the attributes defined in the Microprocessor Software Specification (MSS) file.
The Standard C support library consists of the newlib libc, which contains the standard C functions such as strcpy, strcmp.
The math library is an enhancement over the newlib math library libm.a .
These libraries and include files are created in the current project’s lib and include directories respectively. The -I and -L options of mb-gcc should be used to add these directories to its library search paths.

## Slide 23: Xilinx C Library
The Xilinx C library contains the following components:
Xilinx file support functions LibXil File
Xilinx memory file system LibXil Mfs
Xilinx networking support LibXil Net
Xilinx device drivers LibXil Driver
Notes: The structure of LibXil is outlined in the next slide. The user application calls routines implemented in LibXil and/or libm. In addition to the standard C routines supported by libc.a, Xilinx library LibXil contains the following modules:
+ Stream based file system and device access (LibXil File): These sets of libraries allow access to devices and file systems through system routines such as open, close, read and write. It is a simple memory based file system, which allows easy access to data using file based input-output.
+ Networking application support (LibXil Net): EDK provides a simple TCP/IP stack based library, which can be used for network related projects.
+ Device drivers (LibXil Driver): Some of the library modules interact with drivers. These drivers are provided in the EDK and are configured by libgen.

## Slide 24: Structure of LibXil Library
Notes: The standard newlib libc contains dummy functions for most of the operating system specific function calls such as open, close, read, write. These routines are included in the libgloss component of the standard libc library. The LibXil File module contains routines to overwrite these dummy functions. The routines interact with file systems such as Xilinx Memory File System and peripheral devices such as UART, UARTLITE, and GPIO.
LibXil Net routines provide support for networking applications via ethernet. The module LibXil Net needs some support from the file system and hence calls other routines from the LibXil File and/or the LibXil Mfs modules. On the other hand, if an application requires opening files over the network, routines from the LibXil File module will need the support of the LibXil Net.
Libgen is used to tailor the library compilation for a particular project using attributes in the MSS.

## Slide 25: Outline
Introduction
MSS structure & Parameters
Using Libgen
Xilinx Libraries
Summary

## Slide 26: Review Questions
For a given MicroBlaze system, what are the files and directories created by Libgen?
What file is necessary for Libgen to be run, and what are its main sections?
Why should an MSS file refer to the MHS file, and which Parameter is used for this purpose?

## Slide 27: Review Questions
State three of the Processor instance specific parameters and explain their meaning?
How could you run Libgen?
State three of the Libgen options and explain their meaning?
What are the EDK Libraries?

## Slide 28: Answers
For a given MicroBlaze System, what are the files and directories created by Libgen?
  Libgen creates the following files:
    xmdstub.elf
    bootstrap.elf
  Libgen also generates the following directories:
    Include
    lib
    libsrc

## Slide 29: Answers
What file is necessary for Libgen to be run, and what are its main sections?
  Libgen takes and MSS file as input
  The MSS file has three main sections:
    Global Parameters Specifications ( VERSION, HW_SPEC_FILE)
    Processor Parameters Section
    Drivers specification for each IP peripheral instance
Why should an MSS file refer to the MHS file, and which parameter is used for this purpose?
  An MSS refers to the MHS file for Peripherals Memory Offsets Specification. An MHS file is specified within the global parameters section using the parameter: HW_SPEC_FILE

## Slide 30: Answers
State three of the Processor instance specific parameters and explain their meaning?
  STDOUT: specifies that the peripheral is the standard output
  BOOT_PERIPHERAL: defines the Boot peripheral
  EXECUTABLE: specifies the name and the location of the *.elf executable file for a given MicroBlaze processor instance
How could you run Libgen?
  From a Xygwin Shell using the following command line: libgen [options] filename.mss
  From XPS: Tools  Generate Libraries

## Slide 31: Answers
State three of the Libgen options and explain their meaning?
  -a, -arch: Specify the FPGA Architecture : virtex2pro/virtex2/virtexe/virtex/spartan2/spartan2e
  -s, -stub: Creates the stub files (for MicroBlaze) and BRAM initialization script. Using this option prevents the generation of libraries and drivers
  -m, -mode: This option is Global, allows libgen to be run in one of the following modes: executable (default mode), xmdstub, or bootstrap. It is applied to all the MicroBlaze instances you may have in your project. To have different modes for each processor instance, use the Options:
    -xmdstub proc_inst_name_1 [, proc_inst_name_2, ...]
    -bootstub proc_inst_name_1 [, proc_inst_name 2, ...]
    -executable proc_inst_name_1 [, proc_inst_name_2, ...]

## Slide 32: Answers
What are the EDK Libraries?
  The Embedded Developers Kit provides three libraries:
  Math Library (libm)
  Standard C language support (libc)
  Xilinx drivers and libraries (libxil): Xilinx C Libraries and contain the following:
    Xilinx file support functions LibXil File
    Xilinx memory file system LibXil Mfs
    Xilinx networking support LibXil Net
    Xilinx device drivers LibXil Driver

## Slide 33: Summary
The MSS is the heart of the MicroBlaze System Software & Firmware development
The Library Generator simplifies the System Firmware Design and pre-configures the drivers for every instance of the MicroBlaze system
The Embedded Developers Kit provides libraries and drivers to make software development and integration of the System Firmware much easier