## Slide 1: MicroBlaze System Implementation

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the MicroBlaze™ soft processor core and its advantages
Describe the FPGAs supported by the MicroBlaze soft processor
Specify the Embedded System Tools architecture
Describe the MicroBlaze PSF
Describe the tools used in a MicroBlaze EDK Flow

## Slide 3: Outline
What is the MicroBlaze Soft Processor Core?
Toolset Needed to Develop a MicroBlaze System
MicroBlaze PSF
How to Use the EDK Tools to Build a MicroBlaze System

## Slide 4: What is ?
The MicroBlaze™ soft processor core can be implemented into the Virtex™ family of FPGAs:
  Virtex™
  Virtex™ -E
  Virtex™ -II
  Virtex-II Pro™
  Spartan™ -II
  Spartan™ -IIE

## Slide 5: Overview - PowerPC Compatibility
The MicroBlaze soft processor uses the On Chip Peripheral Bus from IBM’s CoreConnect bus structure
All OPB IP is portable between processors
The MicroBlaze binaries must be recompiled for PPC 405
  Different instruction set
The MicroBlaze soft processor has a very similar ABI to PowerPC
  Ideal for migration to Virtex-II PRO™ devices
Notes: ABI: Application Binary Interface. It is an interface from the Hardware to the Firmware, it defines the Register Files Convention.

## Slide 6: Overview - Basic Statistics
Speed across different devices
  Virtex-II Pro™ (-6), 150 MHz, 101 D-MIPS
  Virtex™ -II (-5), 125 MHz, 82 D-MIPS
  Virtex™ -E (-7), 75 MHz, 49 D-MIPS
  Spartan™ -II (-4), 65 MHz, 43 D-MIPS
  Spartan™ -IIE (-6), 75MHz, 49 D-MIPS
Fastest soft processor for FPGAs
Virtex-II feature utilization
  Embedded multiplier
  SRL 16’s
Around 900 LUTs / 450 Slices
  ~225 CLBs (Virtex, Virtex-E, Spartan-II)
  ~112 CLBs (Virtex-II, Virtex-II PRO)
Notes: For the Virtex-II/Pro FPGA architecture, the MicroBlaze core processor is built using three embedded multipliers; this does not add any extra CLBs to the core size.
32-bit x 32-bit Multiplications in MicroBlaze running on Virtex-II/Pro:
If the input and resultant data types are of type "long" [32 bit], then the multiply instruction takes 3 clock cycles. This multiply takes full advantage of the dedicated multiplier block.
64-bit x 64-bit Multiplications in MicroBlaze running on Virtex-II/Pro:
If the input and resultant data types are of type "long long" [64 bit], then the multiply instruction will take approximately 100 clock cycles.
In devices with Virtex-based architectures (Virtex, Virtex-E, Spartan-II, Spartan-IIE), these multipliers are not available. As a result, all multiply instructions (including long long) in these versions of MicroBlaze will be software multiplies. These software multiplies take a few thousand clock cycles to complete.

## Slide 7: Outline
What is the MicroBlaze Soft Processor Core?
Toolset Needed to Develop a MicroBlaze System
MicroBlaze PSF
How to Use the EDK Tools to Build a MicroBlaze System

## Slide 8: MicroBlaze Tool Set (EDK)
The EDK (Embedded Developers Kit) includes:
  MicroBlaze™ Development Tools Suite
  MicroBlaze Soft CPU
  Standard Peripheral Set
    Timer/Counter, UART lite, Interrupt controller, GPIO, watchdog timer, OPB bus arbiter, External Memory Controller, SPI & ZBT RAM interface, etc.
    Complete documentation with examples
Notes: Additionally, in the EDK, a full Toolset for PowerPC/Virtex-II Pro is included.

## Slide 9: Overview - Design Flow
Minimum tool set to complete a design
  EDK v3.1 or greater
    Includes XygWin
  ISE 5.1i or greater (XST synthesis included)
    XST 5.1i is supported for top-level synthesis
    Synplify/Pro 7.0 is supported for top-level synthesis
    Other synthesis products are on the roadmap
  ModelSim 5.5c supported for hardware simulation
Notes: For the MicroBlaze System Simulation ModelSim XE 5.5.c is also supported. The MicroBlaze soft processor does not use swift models for functional simulation.

## Slide 10
Overview - Design Flow

## Slide 11: Outline
What is the MicroBlaze Soft Processor Core?
Toolset Needed to Develop a MicroBlaze System
MicroBlaze PSF
How to Use the EDK Tools to Build a MicroBlaze System

## Slide 12
MicroBlaze PSF
The Platform Specification Format (PSF) defines:
The compatible set of infrastructure files for a EDK tool release
The infrastructure files are:
  BBD: Black Box Definition
  MDD: Microprocessor Driver Definition
  MHS: Microprocessor Hardware Specification
  MPD: Microprocessor Peripheral Definition
  MSS: Microprocessor Software Specification
  MVS: Microprocessor Verification Specification
  PAO: Peripheral Analysis Order
The Version Scheme
Notes: - The Black Box Definition (BBD) file manages the file locations of optimized hardware netlists for the black box sections of your peripheral design.
- An MDD file contains directives for customizing software drivers.
- The Microprocessor Hardware Specification (MHS) file defines the hardware component. An MHS file is supplied by the user as an input to the Platform Generator (Platgen) tool.
- The Microprocessor Peripheral Definition (MPD) file defines the interface of the peripheral.
- An MSS file is supplied by the user as an input to the Library Generator (Libgen). The MSS file contains directives for customizing libraries, drivers and file systems.
- An MVS file is supplied by the user as an input to the Simulation Model Generator (Simgen) tool. The MVS file contains directives for customizing a simulation model for a defined system.
- A PAO (Peripheral Analyze Order) file contains a list of HDL files that are needed for synthesis, and defines the analyze order for compilation.

## Slide 13
MicroBlaze PSF
opb_ip_vi_j_n
data
.
mpd
.
pao
.bbd
opb_ip_vi_j_n
Drivers
Processor
IP2
data
.
mdd
EDK
User
.
mhs
Sysgen Pro
.
mss
XPS
.
mvs
Other Files
Notes: The .mpd, .bbd, .pao, and the .mdd are files defining the OPB IP integration within the EDK. The .mhs, .mvs and the .mss are files defining the user’s system. The .mhs file could be generated by the user using any text editor, or by using Sysgen Pro.

## Slide 14
MicroBlaze PSF
The Version Scheme for MHS, MSS, and MVS:
Set by the parameter: PARAMETER VERSION = i.j.n
  i - major revision
  j - minor revision
  n - patch level
The Version Setting for BBD, MPD, and PAO:
Concatenated to the basename of the data files
  <ipname>_vi_j_n.mpd
  <ipname>_vi_j_n.bbd
  <ipname>_vi_j_n.pao
  <ipname>_vi_j_n.mdd
Notes: The current version is 2.0.0

## Slide 15: Outline
What is the MicroBlaze Soft Processor Core?
Toolset Needed to Develop a MicroBlaze System
MicroBlaze PSF
How to Use the EDK Tools to Build a MicroBlaze System

## Slide 16
Embedded System Tools
Embedded System Tools offered by the EDK:
  Libgen: Libraries and drivers configuration
  GNU based tools for firmware design and debugging
  Platgen: Hardware platform generation
  Simgen: Hardware simulation utility
  Xilinx Platform Studio (XPS) for project management
  Xilinx Microprocessor Debugger (XMD) for interfacing to different debugging targets (MicroBlaze or ISS)

## Slide 17
Xilinx Platform Studio (XPS)
Platgen
Libgen
MB-GCC / MB-GPP
MB-GDB
XMD
Data2BRAM
Xflow (ISE)
Embedded System Tools

## Slide 18
EST - GUI
Create a New Project after launching the XPS

## Slide 19
EST - GUI
Specify the Project:
Name
Directory
MHS file
Target Device
Custom Peripheral
Notes: When creating a Project, and if you already have an MSS File, XPS will prompt you to create a new MSS file or use the existing one.
If your MicroBlaze system contains custom OPB peripherals, you need to specify the repository of your custom peripherals.

## Slide 20
EST - Source Code
To add Source Code:
Select a MicroBlaze Instance
Add Source Files to the Project

## Slide 21
EST - MSS Settings
To set the MSS Parameters:
Select a peripheral Instance
Right click and select S/W Settings

## Slide 22
EST - MSS Settings
From the XPS Menu we can:
Configure the Peripheral Software Settings
Device Drivers
Driver Version
Driver Levels
Assign Interrupt Handlers
Notes: To configure the device drivers:
- Select the device from the list: System BSP
- Right click on the Particular Device to configure
- Then you will fill the Menu in the above slide

## Slide 23
EST – Compiler
Setting Compiler Options from XPS:

## Slide 24
Setting Compiler Options from XPS:
Environment Tab:
  Compiler
  Flow Setting
EST - Compiler Options
Notes: The Options entered through this menu are applied to all the Processor instances in your system.

## Slide 25
Processor instance Software Settings:
Right click on Processor Instance
Select S/W Settings
EST - S/W Settings

## Slide 26
Processor Property Tab:
Processor Driver
Driver Version
Interface Level
Compilation Mode
STDIN/STDOUT
Debug Peripheral
Boot Peripheral
EST - S/W Settings

## Slide 27
Optimization Tab:
Optimization Level 1/2/3 (-O)
Global Pointer Optimization (-mxl-gp-op)
Generate Mul Inst. (-mno-xl-soft-mul)
Create Symbols for debugging (-g)
EST - Compiler

## Slide 28
Directories Tab:
Location of Library files (-L)
Location of Include files (-I)
Linker Script location (when Custom)
Location of the elf file
EST - Compiler

## Slide 29
Details Tab:
Executable start address:
(-defsym_TEXT_START_ADDR=)
Stack Size (-defsym_STACK_SIZE=)
Comma Separated Options
EST - Compiler

## Slide 30
Others Tab:
Non Available from XPS GUI Options: (-N for example)
Libgen Options
EST - Compiler

## Slide 31
EST - Implementation
From the XPS Menu we can:
Set the Implementation options

## Slide 32
Setting Platgen options from XPS:
Do not insert pads (-i)
Hierarchical Mode (-flat)
Synthesis Project (-s 0/2/4)
EST - Platgen

## Slide 33
Setting Simgen options from XPS:
HDL: VHDL or Verilog
ModelSim Libraries Path
EST - Simgen

## Slide 34
Embedded System Tools
From XPS, the following Utilities could be run:
Libgen (Libraries and Drivers configuration)
MB-GCC (Software Compilation)
Platgen (Platform building)
Xflow (Implementation)
XMD (Debug setup and target selection)
MB-GDB (GNU Debugger)
Data2BRAM (Update the bitstream with new firmware)

## Slide 35
Summary
The MicroBlaze™ soft processor is the fastest available for FPGA
The EDK is the Software Development Environment for a MicroBlaze System
XPS is at the heart of the Embedded System Tools
XPS makes the development of a MicroBlaze System very easy to achieve