## Slide 1: Introduction to MicroBlaze Peripherals

## Slide 2: Objectives
After completing this module, you will be able to:
Specify the free MicroBlaze™ peripherals and their function
Specify the function of the MPD, PAO and BBD Files
Describe the differences between EDIF and HDL flows
Describe attributes and how they affect implementation
Explain the concept of drivers and the MDD file

## Slide 3: Outline
MicroBlaze Peripherals
Peripheral Definition
Common Libraries
Summary

## Slide 4: What is a MicroBlaze Peripheral?
A piece of hardware that connects to a bus to provide extra functionality to the system
  UART
  Ethernet
  Arbiter
  Interrupt controller
  Memory controller
  GPIO
UART
GPIO
Memory Controller
Ethernet
Interrupt Controller
Arbiter
Notes: A MicroBlaze peripheral usually attaches to the On-Chip peipheral bus (OPB). The slide above shows some of the peripherals available to you. Peripherals add to a system by providing additional hardware functionality.

## Slide 5: MicroBlaze Peripherals
Some peripherals that come with the EDK:
  Arbiter
  Block RAM Controller
  General Purpose I/O
  Interrupt Controller
  IPIF
  JTAG UART
Memory Controller (EMC)
SPI Controller
Watchdog Timer
Timer
UART Lite
ZBT Controller
The Xilinx Embedded Processor IP Handbook gives full descriptions of each peripheral and how to use it.
Notes: The Embedded Development Kit includes useful peripherals as standard. A list of the peripherals as well as their full datasheet, and usage, is available in the Hardware Reference Guide.

## Slide 6: MicroBlaze Peripherals
Arbiter
Used in Multiple-Master OPB systems
Controls access to the OPB
Detects OPB bus timeouts and resolves them
I
L M
B
I L M B
Arbiter
D O
P
B
OPB Master
MicroBlaze
JTAG UART
UART Lite
GPIO
RS-232
IEEE 1149.1
LMB Bram
D L M
B
EMC
INTC
External Ram
I O
P
B
I/O
Sample System
Notes: The arbiter is a bus peripheral that controls access to the OPB. This can be used in a multiple-master system in order to ensure only one master is controlling the bus at a time. The arbiter can have a fixed or round-robin priority scheme. Additionally, the arbiter performs timeout functions to ensure that the bus is not indefinitely captured by a faulty peripheral.

## Slide 7: MicroBlaze Peripherals
UART Lite / JTAG UART
Used as in input / output device
Communicates by RS-232 or JTAG
Can be a standard I/O (STDIO) or debug device
I
L M
B
I L M B
Arbiter
D O
P
B
OPB Master
MicroBlaze
JTAG UART
UART Lite
GPIO
RS-232
IEEE 1149.1
LMB Bram
D L M
B
EMC
INTC
External Ram
I O
P
B
I/O
Sample System
Notes: The UART devices are generally used for communication off-chip. The UART Lite is an RS-232 protocol receiver/transmitter, whereas the JTAG UART communicates via the IEEE 1149.1 JTAG standard using the FPGA JTAG USER register.
Both UART peripherals can be used with drivers for Standard I/O (STDIO) functions such as print() and scan(). Additionally, they can be used to connect to a debugging stub or for bootstrap mode for uploading code to the processor system.

## Slide 8: MicroBlaze Peripherals
GPIO
Used as a general-purpose input / output peripheral
Configurable width
I
L M
B
I L M B
Arbiter
D O
P
B
OPB Master
MicroBlaze
JTAG UART
UART Lite
GPIO
RS-232
IEEE 1149.1
LMB Bram
D L M
B
EMC
INTC
External Ram
I O
P
B
I/O
Sample System
Notes: The General Purpose Input / Output (GPIO) is a peripheral that allows user I/O access in and out of the system. The direction of communication can be changed at any time with the supplied drivers. The width of the component is generic and is specified in the user’s .MHS file for the system.

## Slide 9: MicroBlaze Peripherals
Interrupt Controller
Expands the number of interrupts MicroBlaze™ soft processor can handle
Level / edge sensitive
Up to 32 interrupts
I
L M
B
I L M B
Arbiter
D O
P
B
OPB Master
MicroBlaze
JTAG UART
UART Lite
GPIO
RS-232
IEEE 1149.1
LMB Bram
D L M
B
EMC
INTC
External Ram
I O
P
B
I/O
Sample System
Notes: The interrupt controller allows the system to have multiple interrupts with programmable sensitivity, wither to the edge, or level of a signal. More information about this and all other Xilinx-supplied peripherals can be found in the Hardware Reference Guide.

## Slide 10: MicroBlaze Peripherals
External Memory Controller
Interfaces to external Flash / SRAM
Up to 8 memory banks
Address mapable
I
L M
B
I L M B
Arbiter
D O
P
B
OPB Master
MicroBlaze
JTAG UART
UART Lite
GPIO
RS-232
IEEE 1149.1
LMB Bram
D L M
B
EMC
INTC
External Ram
I O
P
B
I/O
Sample System
Notes: The External Memory Controller (EMC) allows easy access to standard FLASH and SRAM memory devices. The timing and the access to the memory is controlled by passing attributes to the peripheral. External memory gets mapped to the microprocessor memory space and can be used transparently by the system for code and/or data.

## Slide 11: Outline
MicroBlaze Peripherals
Peripheral Definition
Common Libraries
Summary

## Slide 12: Peripheral Definition
A peripheral consists of:
Bus connections
Settings
Custom I/O
Source code
Drivers
E.g., GPIO
OPB Bus
I/O Width
User I/O Pins
VHDL
read / write
E.g., UART Lite
OPB Bus
Baud rate
TX/RX
VHDL
Outbyte / inbyte
Peripheral specifications are defined in System Interface Format - This consists of files to specify the peripheral, dependencies, drivers, and functionality
Notes: For a peripheral to be included into a microprocessor design, the port and address information needs to be communicated, along with any specific settings required by the peripheral. The System Interface Format is a set of files that communicates these specifications to the Embedded Development Kit tools

## Slide 13: Peripheral Definition
A peripheral can be included in a system as:
  HDL – E.g., GPIO peripheral
  EDIF netlist
  A mixture of the HDL and EDIF
All flows have a MicroProcessor Peripheral Definition (.mpd), to describe bus / I/O connectivity
  HDL peripherals have a Peripheral Analyze Order (.pao) file to specify the HDL to synthesize, and in what order
  EDIF has a Black Box Definition file (.bbd) to specify which netlist to use for a given configuration
  A ‘mixed’ HDL / EDIF peripheral contains both .pao and .bbd files
Notes: The full format of each of the files that make up the SIF format is available in the Xilinx Embedded System Tools Guide. The most important details of each shall be discussed in this presentation.

## Slide 14: Peripheral SIF File Structure
.
vhd
.
vhd
.
vhd
/my_
peripheral
/data
/hdl
/netlist
/simmodels
.
mpd
.
pao
.bbd
.
vhd
.
vhd
.
vhd
.
vhd
.
edn
.
vhd
.
vhd
.
vhd
.
vhd
/my_
peripheral
/Drivers
/Processor
/IP2
Notes: The above picture is an illustration of the hierarchy of an EDK peripheral. We can see that the peripheral is separated into software, and hardware. The software consists of drivers and a driver definition file. The hardware consists of Peripheral Definition files, HDL, netlists and simulation models.

## Slide 15: Peripheral Definition
All installed peripherals are under the Xilinx_EDK Directory
All have an .mpd file in the data directory
Most have VHDL, in the HDL directory, but this is often encrypted IP
Some have EDIF
Notes: MicroBlaze peripherals are often HDL so that the user-specified .mhs file, can parameterize the core during the build. Xilinx uses this flow for most peripherals. However, to protect the IP, these HDL files are encrypted. These files can be read and synthesized by the embedded tools, but cannot be read by the user.
The .mpd file is not encrypted, and so the user can see all the generics and ports used by the peripheral.
By looking at the .mpd file a user should have all of the interfacing information for connecting the peripheral to the MicroBlaze system.

## Slide 16: Peripheral Definition - .mpd
The MicroProcessor Peripheral Definition file defines the interface of a system
  Ports and default connectivity for bus interfaces
  Parameters and default values
Any parameters and default values can be overwritten by the MicroProcessor Hardware Specification file, which defines the system
Notes: The .mpd file contains default information so that the user does not have to change the fields of commonly set attributes. For example, in the UART Lite component, there is a default baudrate and parity control. You would only need to specify the settings for these if they differ from the default. This ensures that the .mhs file is smaller and more readable.

## Slide 17: Peripheral Definition - .mpd
SELECT slave opb_gpio, EDIF=TRUE
# Generics for vhdl or parameters for verilog
CSET attribute C_BASEADDR = 0x20000000, std_logic_vector
CSET attribute C_HIGHADDR = 0x200000FF, std_logic_vector
CSET attribute C_OPB_DWIDTH = 32, integer
CSET attribute C_OPB_AWIDTH = 32, integer
CSET attribute C_GPIO_WIDTH = 32, integer
CSET attribute C_ALL_INPUTS = 0, integer
CSET bus_interface BUS=SOPB, BUS_STD=OPB, BUS_TYPE=SLAVE
# Global ports
CSET signal OPB_Clk = OPB_Clk, in,, ISCLOCK=TRUE
CSET signal OPB_Rst = OPB_Rst, in
# OPB signals
CSET signal OPB_ABus = OPB_ABus, in, [0:C_OPB_AWIDTH-1], BUS=SOPB
CSET signal OPB_BE = OPB_BE, in, [0:C_OPB_DWIDTH/8-1], BUS=SOPB
CSET signal OPB_DBus = OPB_DBus, in, [0:C_OPB_DWIDTH-1], BUS=SOPB
CSET signal OPB_RNW = OPB_RNW, in,, BUS=SOPB
CSET signal OPB_select = OPB_select, in,, BUS=SOPB
CSET signal OPB_seqAddr = OPB_seqAddr, in,, BUS=SOPB
CSET signal GPIO_errAck = Sl_errAck, out,, BUS=SOPB
CSET signal GPIO_retry = Sl_retry, out,, BUS=SOPB
CSET signal GPIO_toutSup = Sl_toutSup, out,, BUS=SOPB
CSET signal GPIO_xferAck = Sl_xferAck, out,, BUS=SOPB
# gpio signals
CSET signal GPIO_IO = "", inout, [0:C_GPIO_WIDTH-1], ENABLE=MULTI
END
Attributes
Bus Address Range
Signals
No default signal name
Default signal name
Peripheral Type

## Slide 18: Common .mpd Commands
Select
  Specifies peripheral type, name, and configuration
Cset Attributes
  HDL Flow - Get passed into the HDL as generic parameters
  EDIF Flow - Can be used in the .bbd as a lookup table parameter
Cset Signals
  Specifies the signals (in, out, bidirectional) that connect to the peripheral
SELECT slave opb_gpio, EDIF=TRUE
CSET attribute C_BASEADDR = 0x20000000, std_logic_vector
CSET signal OPB_ABus = OPB_ABus, in, [0:C_OPB_AWIDTH-1], BUS=SOPB
Notes: The MicroProcessor Peripheral Definition (.mpd) file is an ASCII user-editable file. The main commands are listed above. The full syntax information for the .mpd file is available in the Hardware Reference Guide.

## Slide 19: Peripherals – The .pao File
The Peripheral Analyse Order file contains a list of HDL files that are needed for synthesis
Additionally, it defines the analyze order for compilation
lib common_v1_00_a common_types_pkg
lib common_v1_00_a pselect
lib opb_gpio_v1_00_a gpio_core
lib opb_gpio_v1_00_a opb_gpio
Library Name
Hdl File to include
Common Functions Supplied with MDK
Users HDL files in Analyze order
Notes: For a VHDL flow, the synthesizer shall compile the following files to the following libraries, in this order:
common_types_pkg.vhd -> common_v1_00_a
pselect.vhd -> common_v1_00_a
gpio_core.vhd -> opb_gpio_v1_00_a
opb_gpio.vhd -> opb_gpio_v1_00_a

## Slide 20: Peripherals – The .bbd File
The Black Box Definition file manages the file locations of optimized hardware netlists for black-box peripherals
It is a look-up table that lists netlist files
C_FAMILY CONFIGURATION Files
#############################################################
virtex 1 virtex/my_ip_1.edf
virtex 2 virtex/my_ip_2.edf
virtex 3 virtex/my_ip_3.edf
virtex 4 virtex/my_ip_4.edf
virtex 5 virtex/my_ip_5.edf
virtex 6 virtex/my_ip_6.edf
spartan2 1 spartan2/my_ip_1.edf
spartan2 2 spartan2/my_ip_2.edf
spartan2 3 spartan2/my_ip_3.edf
spartan2 4 spartan2/my_ip_4.edf
spartan2 5 spartan2/my_ip_5.edf
spartan2 6 spartan2/my_ip_6.edf
Lookup Table Header
Comparison Fields
Configuration Netlists
Lookup
Table
Notes: E.g.,: If the user selects
C_FAMILY=VIRTEX
CONFIGURATION=6
virtex/my_ip_6.edf shall be included in the project. This shall be placed in the projects /implementation directory.

## Slide 21: Peripherals – Defining the Drivers
The MicroProcessor Driver Definition file contains directives for customising software drivers
Used by the Library Generator (Libgen) to customize the driver depending on different options in the software specification
Only really of interest when generating custom peripherals

## Slide 22: Peripherals – Defining the Drivers
BEGIN driver XUartLite
constant VERSION = 2.0.0 # uses SIF 2.0.0
parameter LEVEL = 0 # default level
END
BEGIN level 0
constant INBYTE = XUartLite_RecvByte, DEFINED_IN = xuartlite_l
constant OUTBYTE = XUartLite_SendByte, DEFINED_IN = xuartlite_l
constant COPYFILES = (xuartlite_l.c xuartlite_l.h Makefile)
constant DEPENDS = (common_v1_00_a)
constant CONFIG_INCLUDE = xparameters, VALUES = ( NUM_INSTANCES C_BASEADDR )
parameter INT_HANDLER = XIntc_DefaultHandler, INT_PORT = Interrupt
END
BEGIN level 1
constant COPYFILES = ALL
constant DEPENDS = (common_v1_00_a)
constant CONFIG_INCLUDE = xparameters, VALUES = ( NUM_INSTANCES C_BASEADDR DEVICE_ID )
constant CONFIG_FILE = xuartlite_g, VALUES = ( DEVICE_ID C_BASEADDR )
parameter INT_HANDLER = XUartLite_InterruptHandler, INT_PORT = Interrupt
END
Level 1 - OS-level Drivers
STDIO Drivers
C files to copy into system project
Driver Dependencies
Preprocessor configurations
Interrupt service rouine
Full details of the .mdd file format can be found in the Embedded System Tools Guide

## Slide 23: Outline
MicroBlaze Peripherals
Peripheral Definition
Common Libraries
Summary

## Slide 24: Common Libraries
The EDK includes some useful VHDL libraries
Optimized functionality
Common MicroProcessor functions
  Multiplexers - (Mux_encode_sel, Mux_onehot)
  Gates - (or_bits, or_gate)
  Address Decoders - (pselect , pselect_top)
Notes: The MicroBlaze install has some library VHDL, which is used by peripherals and can also be used by your custom peripherals. This code is not encrypted and can be viewed by the user.

## Slide 25: Common Libraries
Pselect.vhd - Parameterizable Peripheral Select (Address Decoder)
generic (
C_AB : integer := 9;
C_AW : integer := 32;
C_BAR : std_logic_vector(0 to 31) := X"33000000"
);
port (
A : in std_logic_vector(0 to C_AW-1);
AValid : in std_logic;
PS : out std_logic
);
end entity pselect;
Example Pselect implementation for decoding the address range 0xFFFF8000 to 0xFFFF803F
C_AB = number of address bits to decode
C_AW = width of address bus
C_BAR = base address of peripheral
Optimized for Xilinx
Architectures (MuxCY)
Notes: Pselect is a particularly useful peripheral as it is an address decoder. The address value and the width can be parameterized by the peripheral, which can be propogated from the applications .MHS file. The address decoder is very optimal using fast Virtex carry logic to make this combinatorial function as fast as possible

## Slide 26: Outline
MicroBlaze Peripherals
Peripheral Definition
Common Libraries
Summary

## Slide 27
Skills Check

## Slide 28: Review Questions
The JTAG UART and UART Lite can perform two functions. What are they?
Which configuration file is required for all peripherals?
What extra file is required for HDL flows ? for EDIF flows?
Using the .BBD slide, which netlist is selected if the .mhs file has :
  C_FAMILY=Virtex Configuration=3?
What is the purpose of Pselect?

## Slide 29: Answers
The JTAG UART and UART Lite can perform two functions. What are they?
  It can run as a STDIO (Standard I/O Peripheral) and also as a debug peripheral
Which configuration file is required for all peripherals?
  Every peripheral has a Microprocessor Peripheral Definition (.mpd) file. This specifies the ports and attributes that can be set for the peripheral along with default signal assignments
What extra file is required for HDL flows?
  A Peripheral Analyze Order (.pao) file. This specifies the HDL files to be included and their analyze order

## Slide 30: Answers
What extra file is required for EDIF flows?
  A Black-Box Description (.bbd) file specifies a lookup table of parameters and netlists to use
Using the .BBD slide, which netlist is selected if the .mhs file has : C_FAMILY=Virtex Configuration=3?
  virtex/my_ip_3.edf
What is the purpose of Pselect?
  It is a Xilinx-optimized Address Decoder for peripherals, which is included in most MicroBlaze peripherals

## Slide 31: Summary
The Embedded Development Kit comes with many peripherals that can be used in custom systems
The MicroProcessor Peripheral Definition (.mpd) file specifies the ports and attributes for a peripheral
The Black Box Description File (.bbd) specifies a lookup table of netlists to be used for a said configuration
The Peripheral Analyze Order (.pao) file specifies the HDL to be included, the libraries they come from and the order to analyze them
The MicroProcessor Driver Definition (.mdd) file specifiy and parameterize drivers for peripherals
The common libraries have useful architectures for use in peripherals