## Slide 1: Platgen
The Platform Generator

## Slide 2: Objectives
After completing this module, you will be able to:
Describe the function of the Platform Generator
Understand the MHS structure and the different attributes
Use the Platform Generator

## Slide 3: Outline
Introduction
MHS Structure & Attributes
Using Platgen
Summary

## Slide 4: What is Platgen
Microprocessor Platform Generator
Generates the netlists required to construct a microprocessor in Xilinx silicon
Creates support files required by synthesis by Xilinx and 3rd party tools
Does not deal with software components of a microprocessor system
Notes: Platgen is the tool used to generate the system platform. It only deals with the hardware aspects of the system, leaving firmware insertion to the Xilinx implementation tools.
The outputs of the system include netlists to build the microprocessor system and support files.
These support files consist of a VHDL wrapper file for inclusion in a VHDL project. Additionally, output project files are available for either XST or Synplicity.

## Slide 5: What is Platgen
Inputs:
  Microprocessor Hardware Specification (.mhs) file
  Text file specifying the masters, slaves. and arbiters that make up the microprocessor system
  HDL and EDIF netlists for Xilinx-provided, and custom peripherals
Outputs
  Edif netlists for generated peripherals
  Toplevel HDL wrapper file
  Synthesis project file
  Flattened system netlist
  Block RAM Memory Map (.bmm)
Notes: The Microprocessor Hardware Specification Files (.mhs) is the primary input to Platgen. This file specifies the hardware configuration to use.
Once this file is read, peripherals are loaded into the system. These can be in the form of HDL or EDIF netlists.
Platgen outputs the EDIF netlists of the generated system and a HDL wrapper. Alternatively, the whole design can be flattened for top-level implementation without further synthesis.

## Slide 6: Outline
Introduction
MHS Structure & Attributes
Using Platgen
Summary

## Slide 7: What is an MHS File
The Microprocessor Hardware Specification (.mhs) defines the hardware component:
  Bus architecture: (OPB, LMB, others in Virtex-II Pro)
  Peripherals :(E.g., UART, GPIO, EMAC)
  Processor(s): (E.g., MicroBlaze, PPC)
  System connectivity
  Interrupt priorities
  Address space
Notes: The Microprocessor Hardware Specification file defined the connectivity of the hardware system. This can include multiple processors and bus structures, as well as interrupt controllers and peripherals.

## Slide 8: MHS File Syntax
Attributes have priority over the equivalent .mpd file
MHS file only needs to specify signals with no defaults and attributes that need to change
BEGIN opb_uartlite
PARAMETER C_BASEADDR = 0xffff0200
PARAMETER C_HIGHADDR = 0xffff02ff
PARAMETER INSTANCE = myuart
PARAMETER HW_VER = 1.00.b
PARAMETER C_DATA_BITS = 8
PARAMETER C_CLK_FREQ = 100000000
PARAMETER C_BAUDRATE = 19200
PARAMETER C_USE_PARITY = 0
PORT RX = rx
PORT TX = tx
BUS_INTERFACE SOPB = opb_bus
END
# Generics for vhdl or parameters for verilog
PARAMETER C_BASEADDR = 0xFFFF8000, DT=std_logic_vector
PARAMETER C_HIGHADDR = 0xFFFF80FF, DT=std_logic_vector
PARAMETER C_OPB_DWIDTH = 32, DT=integer
PARAMETER C_OPB_AWIDTH = 32, DT=integer
PARAMETER C_DATA_BITS = 8, DT="integer range 5 to 8"
PARAMETER C_CLK_FREQ = 125_000_000, DT=integer
PARAMETER C_BAUDRATE = 9600, DT=integer
PARAMETER C_USE_PARITY = 1, DT=integer
PARAMETER C_ODD_PARITY = 1, DT=integer
# Global ports
PORT OPB_Clk = "", DIR=IN, SIGIS=CLK, BUS=SOPB
PORT OPB_Rst = OPB_Rst, DIR=IN, BUS=SOPB
PORT Interrupt = "", DIR=OUT, EDGE=RISING, SIGIS=INTERRUPT
# OPB slave signals
PORT OPB_ABus = OPB_ABus, DIR=IN, VEC=[0:C_OPB_AWIDTH-1], BUS=SOPB
PORT OPB_BE = OPB_BE, DIR=IN, VEC=[0:C_OPB_DWIDTH/8-1], BUS=SOPB
PORT OPB_RNW = OPB_RNW, DIR=IN, BUS=SOPB
PORT OPB_select = OPB_select, DIR=IN, BUS=SOPB
PORT OPB_seqAddr = OPB_seqAddr, DIR=IN, BUS=SOPB
PORT OPB_DBus = OPB_DBus, DIR=IN, VEC=[0:C_OPB_DWIDTH-1], BUS=SOPB
PORT UART_DBus = Sl_DBus, DIR=OUT, VEC=[0:C_OPB_DWIDTH-1], BUS=SOPB
PORT UART_errAck = Sl_errAck, DIR=OUT, BUS=SOPB
PORT UART_retry = Sl_retry, DIR=OUT, BUS=SOPB
PORT UART_toutSup = Sl_toutSup, DIR=OUT, BUS=SOPB
PORT UART_xferAck = Sl_xferAck, DIR=OUT, BUS=SOPB
# uart signals
PORT RX = "", DIR=IN
PORT TX = "", DIR=OUT
END
Overridden
Overridden
Overridden
.mhs entry
Uartlite .mpd entry
Notes: The MHS file consists of global settings and entries between BEGIN  END separators. The peripheral is defined, and then parameters and ports specified.
It should be noted that the MHS file entries for a peripheral correspond to the .MPD file (see Peripherals presentation) for the peripheral. If a parameter is redefined, then this setting takes priority over the settings in the mpd file and shall affect the construction of the peripheral. Conversely, if a parameter or port is not specified in the MHS file, then the values in the MPD file shall be used.

## Slide 9: MHS File Example
# Parameters
PARAMETER VERSION = 2.0.0
# Global Ports
PORT sys_reset = sys_reset, DIR = input
PORT sys_clk = sys_clk, DIR = input
PORT rx = rx, DIR = input
PORT tx = tx, DIR = output
PORT leds = leds, DIR = inout, VEC = [0:3]
Version Control - EDK3.1 Uses MHS version 2.0.0
Global (Microprocessor Toplevel) Port declarations
Global signals can be tied to VCC or GND with the keywords net_vcc or net_gnd
Notes: The first entry in an MHS file should be the version of the file. In the case of EDK 3.1, the version should be set to 2.0.0.
Global ports are not localized between a BEGINEND construct, and so are the I/O of the system.
All I/O should be defined globally. Signals can be tied to VCC or GND using the signal names specified in this slide. Please note that these are reserved names and should not be assigned to outputs.

## Slide 10: MHS File Example
#####################
# Instantiate busses
#####################
BEGIN opb_v20
PARAMETER HW_VER = 1.00.b
PARAMETER INSTANCE = opb_bus
PORT SYS_Rst = sys_reset
PORT OPB_Clk = sys_clk
END
BEGIN lmb_v10
PARAMETER INSTANCE = d_lmb
PARAMETER HW_VER = 1.00.a
PORT LMB_Clk = sys_clk
PORT SYS_Rst = sys_reset
END
BEGIN lmb_v10
PARAMETER INSTANCE = i_lmb
PARAMETER HW_VER = 1.00.a
PORT LMB_Clk = sys_clk
PORT SYS_Rst = sys_reset
END
All bus and peripheral definitions are defined between a BEGIN-END block
Notes: All peripheral definitions have their parameter and port definitions in local scope. After the begin keyword, the peripheral name is specified.
Each peripheral, Master, or Bus, must have its own unique name. This is specified with the INSTANCE keyword.
The version of the peripheral to use is specified with the HW_VER keyword.
Signals that are not assigned in the MPD file, or whose assignment should be changed, are also specified.

## Slide 11: MHS File Example
#######################################
# Instantiate memory
#######################################
BEGIN lmb_lmb_bram_if_cntlr
PARAMETER INSTANCE = mylmblmb_cntlr
PARAMETER HW_VER = 1.00.a
PARAMETER C_BASEADDR = 0x00000000
PARAMETER C_HIGHADDR = 0x00001fff
BUS_INTERFACE ILMB = i_lmb
BUS_INTERFACE DLMB = d_lmb
BUS_INTERFACE PORTA = porta
BUS_INTERFACE PORTB = portb
END
BEGIN bram_block
PARAMETER INSTANCE = bram1
PARAMETER HW_VER = 1.00.a
BUS_INTERFACE PORTA = porta
BUS_INTERFACE PORTB = portb
END
###################################
# Instantiate OPB peripherals: gpio, uartlite
###################################
BEGIN opb_uartlite
PARAMETER INSTANCE = myuart
PARAMETER HW_VER = 1.00.b
PARAMETER C_DATA_BITS = 8
PARAMETER C_CLK_FREQ = 100000000
PARAMETER C_BAUDRATE = 19200
PARAMETER C_USE_PARITY = 0
PARAMETER C_BASEADDR = 0xffff0200
PARAMETER C_HIGHADDR = 0xffff02ff
PORT RX = rx
PORT TX = tx
BUS_INTERFACE SOPB = opb_bus
END
BEGIN opb_gpio
PARAMETER INSTANCE = mygpio
PARAMETER HW_VER = 1.00.a
PARAMETER C_GPIO_WIDTH = 4
PARAMETER C_ALL_INPUTS = 0
PARAMETER C_BASEADDR = 0xffff0100
PARAMETER C_HIGHADDR = 0xffff01ff
PORT GPIO_IO = "leds"
BUS_INTERFACE SOPB = opb_bus
END
Notes: The Block RAM controller on the LMB specifies the size of the local memory space.
Parameters are also used to set generics within the VHDL code of the peripherals to be synthesized. In the UART_LITE component, the baudrate and parity bits are set in the MHS.
Additionally, all peripherals have their address range specified. This is usually passed to the Pselect common library module (see custom peripheral module) for address decoding.

## Slide 12: Outline
Introduction
MHS Structure & Attributes
Using Platgen
Summary

## Slide 13: Sample Platgen Command line
Platgen –a <architecture> <-flat> <-i> <-P peripheral dir> <-s 0,2,4> <filename.mhs>
FPGA Architecture to target:
Virtex, virtexe, spartan2, spartan2e, virtex2, virtex2pro
mhs input file
Custom Peripheral Repository
Synthesis tool (none, xst, synplicity)
Add this switch to create a toplevel netlist
Do not insert IO

## Slide 14: Platgen Options
-a (Architecture family)
  Allows you to target a specific architecture family. The default family is Virtex™-II
-flat (Generate a flatten implementation netlist file)
  Generates a flattened implementation netlist file. A synthesis project file is not created
-h (Help)
  The -h option displays the usage menu and quits
-i (Do not insert I/Os at top-level)
  Disables I/O insertion at the top-level. This allows the processor system to be included as a macro in a top-level design. Otherwise, the output from Platform Generator is the top-level design
-l (Specify the HDL format)
  Allows you to specify the HDL format. The default value is vhdl. Options: [vhdl, verilog]

## Slide 15: Platgen Options
-p (Specify the Project Directory)
  Allows you to specify the project directory path. The default is the current directory
-P (Peripheral repository load path)
  Specifies the peripheral repository load path
-s (Generate synthesis vendor project file)
  Produces a synthesis vendor specific project file. The -s option builds the synthesis project file for you of the HDL files that were left untouched in default mode (that is, not specifying the -flat option). Options: [0,2,4] 0 - None 2 - iSE - XST - SCR/PRJ file 4 - Synplicity - Synplify - PRJ file
-v (Display version)
  Displays the version and quits
Notes: By default, Platform Generator runs in hierarchal mode. In hierarchal mode, Platform Generator generates hierarchal implementation netlists. This means that each instance of a defined peripheral in the MHS file is synthesized. The default mode leaves the toplevel HDL file untouched allowing you to synthesize it in any synthesizer of your choice. Currently, Platform Generator only supports XST and Synplify.

## Slide 16: Platgen in XPS
1. Set the platgen options from
optionsproject options
2. Invoke Platgen from the icon

## Slide 17: Platgen Generation
Platgen has a priority mechanism for finding peripherals
  1. Search the ./myip directory
  2. Search the $XIL_MYPERIPHERALS/myip directory
  3. Search $XILINX_EDK/hw/coregen/ip/xilinx/pcores*/com/xilinx/ip2/processor

## Slide 18: Platgen Output Files
Netlists
  Platgen generates one netlist with the -flat option, no synthesis project or VHDL is made
  Without the -flat option, netlists are made for each submodule with a toplevel HDL wrapper file. Synthesis projects are made with the -s switch. Any HDL peripherals can have this HDL loaded into the synthesis tool also (see Peripheral module)
BMM – Block RAM Memory Map
  Specifies the on-chip memory map. This is used with the implementation tools to specify the RAM blocks to put the ELF into
Notes: Example bram_init.bmm file for a Virtex2 device.
ADDRESS_BLOCK bram0 RAMB16 [0x00000000:0x00007FFF] BUS_BLOCK bram0_bram_block_0_i_ramb16_s2_s2_0 [31:30] PLACED = X2Y5; bram0_bram_block_0_i_ramb16_s2_s2_1 [29:28] PLACED = X3Y6; bram0_bram_block_0_i_ramb16_s2_s2_2 [27:26] PLACED = X1Y5; bram0_bram_block_0_i_ramb16_s2_s2_3 [25:24] PLACED = X3Y7; bram0_bram_block_0_i_ramb16_s2_s2_4 [23:22] PLACED = X1Y7; bram0_bram_block_0_i_ramb16_s2_s2_5 [21:20] PLACED = X1Y6; bram0_bram_block_0_i_ramb16_s2_s2_6 [19:18] PLACED = X2Y4; bram0_bram_block_0_i_ramb16_s2_s2_7 [17:16] PLACED = X2Y6; bram0_bram_block_0_i_ramb16_s2_s2_8 [15:14] PLACED = X3Y4; bram0_bram_block_0_i_ramb16_s2_s2_9 [13:12] PLACED = X3Y8; bram0_bram_block_0_i_ramb16_s2_s2_10 [11:10] PLACED = X3Y3; bram0_bram_block_0_i_ramb16_s2_s2_11 [9:8] PLACED = X3Y5; bram0_bram_block_0_i_ramb16_s2_s2_12 [7:6] PLACED = X1Y4; bram0_bram_block_0_i_ramb16_s2_s2_13 [5:4] PLACED = X1Y3; bram0_bram_block_0_i_ramb16_s2_s2_14 [3:2] PLACED = X2Y7; bram0_bram_block_0_i_ramb16_s2_s2_15 [1:0] PLACED = X2Y3; END_BUS_BLOCK; END_ADDRESS_BLOCK;
Added through implementation (not by platgen) to create bram_init_bd.bmm
HDL instance name for block RAM
Address Bits
RAM block name
Address range

## Slide 19: Outline
Introduction
MHS structure & Attributes
Using Platgen
Summary

## Slide 20: Review Questions
What are the inputs to platgen ?
What are the outputs to platgen
  With the -flat switch?
  Without this switch?
What software should be run after platgen
  With the -flat switch?
  Without the -flat switch?
What output file specifies the memory configuration to the implementation tools ?

## Slide 21: Answers
What are the inputs to platgen?
  The Microprocessor Hardware Specification file. This file specifies the structure of the hardware to be generated
  The peripheral repositories, both custom and Xilinx-supplied
What are the outputs to platgen
  With the -flat switch?
    A toplevel netlist and bmm file only
  Without this switch?
    A vhdl wrapper file, and netlists, or VHDL for each peripheral, and a bmm file

## Slide 22: Answers
What software should be run after platgen
  With the -flat switch?
    The netlist for the toplevel has been created, so implementation (ISE or XFLOW) can be run without further synthesis
  Without the -flat switch?
    The synthesis project should be run to generate the toplevel design
What output file specifies the memory configuration to the implementation tools?
  The BMM file specifies the instance names and address map of the block RAMs for annotation through the implementation flow.

## Slide 23: Summary
The Platform Generator creates the microprocessor system hardware
This can be the toplevel of the design or instantiated within a higher toplevel
The MHS file specifies the hardware to be built
Synthesis projects for XST and Synplicity can be generated
Platgen does not deal with the user firmware in any way