## Slide 1: Debugging Software
MB-GDB & XMD

## Slide 2: Objectives
After completing this module, you will be able to:
Understand the MicroBlaze™ debugging options
Understand how the debugger (MB-GDB) works
Use the MicroBlaze debugger to debug a design
  Using a remote hardware target
  Using an Instruction Set Simulator
Notes: We will present a definition of software intrusive debugging and hardware debugging.

## Slide 3: Outline
Introduction
Using the Debugger
Intrusive Debugging
Instruction Set Simulation
Summary

## Slide 4: Tool Definitions
GDB
  GNU debugger
    GUI interface to the debugger
    Loads and executes your program in a variety of manners
    Monitors and updates the memory and registers
XMD
  Xilinx Microprocessor Debug Engine
    Command line program
    Connects to mb-gdb via TCP/IP
    Allows for several different debugging targets
      Remote hardware running XMD -stub via UART
      Instruction Set Simulation
Notes: XMD controls communication between the hardware system and GDB.
MB-GDB is a variant on the GNU based debugger, GDB. It was made by Xilinx to help debug programs that run on the MicroBlaze™ soft processor.
The debugger allows you a look “inside” the processor while a program is running by showing the contents of registers and memory. It also gives you a snapshot of the processor at the moment a program failed.
MB-GDB also allows you to change register and memory contents, which enables experimenting and correcting the effects of a bug.
XMD is a debug engine. It is used for debugging with an Instruction Set Simulator and software intrusive debugging with JTAG or xmd-stub.

## Slide 5: Tool Definitions
xmdstub
  Executable that resides in lower memory of MB system
    Allows software control and monitoring of registers and memory
    Makes remote hardware debugging possible
    Communicates to XMD via UART
Notes: XMD-stub is compiled along with the MicroBlaze™ system and is, initially, the only program running in memory. It provides the debugger the ability to load new programs and then monitor and update register and memory contents of those programs to be debugged.

## Slide 6: Debugging Terminology
Intrusive Software Debugging
  Intrusive because it requires xmdstub to be running in lower memory on a hardware board
  Also requires a UART OPB peripheral and a remote hardware target
  Communication between XMD and xmdstub can be with either a serial cable or a JTAG cable
Instruction Set Simulation (ISS)
  Host program that models the processor to execute the program under test
  No hardware target required
Notes: Software debugging requires lower memory (block RAM) to retrieve and load data. Software debugging also requires a UART to be placed on the design’s OPB bus, which will require additional FPGA resources. XMD stub uses a little less than 1kB.
ISS works with a model of the processor. A cycle accurate ISS will execute instructions in the precise number of clock cycles necessary to perform it, but note it does not know the actual timing delays.

## Slide 7: Software Intrusive Debugging
UART
OPB
Instruction Memory (BRAM)
xmd stub
mb-gdb
Serial Cable or
JTAG Cable
TCP/IP
XMD
PC
Lab Workstation
Hardware/ Protyping Board
FPGA
Notes: Software intrusive debugging allows you to debug your design while it is running on the FPGA. This type of debugging requires that a software stub (XMD-stub) already be running on the MicroBlaze™ microprocessor in the FPGA.
The XMD-stub must be incorporated in the design by selecting its option when the design is compiled by the GNU C compiler (gcc). This compiler option changes the base memory address of the executable program so it is placed above the XMD-stub.
XMD-stub will place additional instructions in the block RAMs of the FPGA so that the contents of the MicroBlaze registers and memory locations can be uploaded. XMD-stub will also require a UART to be placed on your data side OPB bus.
Note that the use of the TCP/IP cable is not required if you are going to have XMD running on the same machine as MB-gdb. Debugging with JTAG has the same debugging capabilities as debugging with XMD-stub. The JTAG logic is used to retrieve/send data used for debugging through the JTAG cable. The JTAG implementation requires a UART to be placed on the OPB.

## Slide 8: Simple ISS
Simple ISS
  Uses mb -gdb
    Design must be compiled with the debugging information necessary to communicate with mb-gdb
    Simple ISS is used to determine whether the design is functionally correct
    No interaction with hardware
mb-gdb
PC
ISS
Notes: Simulation and the ISS model what the processor would do with the instructions provided.
Mb-gcc -g -xl -mode -executable -L ./lib program.c ...creates a MicroBlaze executable called a.out with the debugging information needed by mb-gdb.
Note that the program must NOT access any peripherals and can only access the Local Memory Bus (LMB) address space.

## Slide 9: Cycle Accurate ISS
Cycle Accurate ISS
  Uses mb -gdb
    Design must be compiled with the debugging information necessary to communicate with GDB
    XMD must be running
    It executes each instruction in a single execution step and uses detailed information about the pipeline behavior of the processor to provide cycle count information
    No interaction with hardware
XMD
ISS
PC
mb-gdb
Notes: Use of ISS in a cycle accurate simulation models what the processor would do with the instructions provided.
XMD% mbconnect sim
…this is a sample command line for invoking XMD using the cycle accurate ISS as the target. Now mb-gdb can connect to xmd. Load mb -gdb with the a.out file created earlier (a.out was made with the Mb-gcc -g -xl -mode -executable -L ./lib program.c command) and connect to the target from the mb-gdb window.
Since ISS does not model the behavior of any peripheral, the program must not access any peripherals or any memory beyond the local memory address space.

## Slide 10: Outline
Introduction
Using the Debugger
Intrusive Debugging
Instruction Set Simulation
Summary

## Slide 11: How to Use GDB
Load Executable
Set Debugging Target
Notes: To connect to XMD (software intrusive debugging or cycle accurate simulation), set debug target to Remote/TCP (if xmd is running on a remote machine. If it is on the same PC use the Simulator option) . Remember, the connection between XMD and GDB can be a TCP/IP cable. This allows for debugging over a network. XMD can be running in the lab and GDB can connect to it over a TCP/IP network. Note that this slide also shows that the ISS simulator is a valid target.
GDB executes your program in a variety of manners: single step, run to completion, run until a breakpoint or watch point is reached. This allows you to examine the memory and register when your program has stopped.
Note that the debuggers use is target independent -- same commands regardless of method of debugging.

## Slide 12: How to Use GDB
Run Program under test
Single Step
View Registers
View Memory
Set Breakpoints
Breakpoint
Notes: You can view 32 MicroBlaze™ registers and the control registers (program counter and machine status register).
The GDB allows users to execute their instructions step by step. Single step simulates instructions line by line. Setting a breakpoint stops the debugger at a particular instruction. Stepping is execution of one “step”of the user program, where “step” can mean either one line of source code or one machine instruction.
GDB also allows you to view both the source code and assembly code of the program under test. It also allows you to execute C and assembly code simultaneously (enabling you to see the C code converted to assembly).
View Memory allows you to see the memory map of your entire design.

## Slide 13: Viewing Registers & Memory
Memory Address
ASCII equivalent data
Program Counter
Machine Status Register
Notes: The memory map allows the user to know what is stored in a particular memory location. Memory addresses are in the left-hand column (0x48c). The area to the right converts the machine code to ASCII. This is useful if you store a lot of characters or integers (floating points won’t show up this way).
After the program is loaded or has stopped executing, you can view and modify processor memory, register contents, and local variables.

## Slide 14: Outline
Introduction
Using the Debugger
Intrusive Debugging
Instruction Set Simulation
Summary

## Slide 15: Setting Up xmdstub
xmdstub is necessary for intrusive software debugging:
  MSS file
    Must contain the XMDSTUB attribute
  libgen
    Compiles the xmdstub
  platgen
    Builds the system and creates the BMM file
    A netlist is generated
mb -gcc -g -xl -mode -xmdstub program.c
  Local memory is initialized with the xmdstub executable
Bitgen / Data2BRAM
  Links the Software (.elf file) to the hardware
Notes: XMD -stub is used to control execution of the test program and provide communication between the debugging host (XMD) and the board executing the test program.
The entire flow must be run with the XMD -stub option so the compiler can offset the address of the program, so that the stub is in local memory. Libgen delivers the assembly code for XMD-stub. Platgen builds the hardware for the MB system.
The UART or JTAG OPB peripheral will be part of the lines of communication for XMD -stub and GDB.
GCC (GNU C compiler) will offset the memory address of the compiled program (using the startup code crt1.o, instead of the default crt0.o) so that it is loaded above the xmdstub in memory. Remember, when the program is loaded, it will be loaded above the stub in memory. (0x400)

## Slide 16: Running XMD
XMD must be running before debugging can begin
  XMD is the Xilinx Microprocessor Debug Engine
  XMD communicates via the UART to xmdstub (in this case, the remote hardware running xmdstub)
  Command line program
Notes: XMD is a command line program that will run in the background, making the connection between the debug target and debugger. This enables the UART to become the terminal display.
Remember that before XMD is started, XMD -stub must be compiled with GCC, the design must be synthesized and implemented (placed and routed for the FPGA), and the device programmed with the bitstream generated by the Xilinx Implementation Tools (ISE).
Once the system is running XMD -stub (design has been downloaded to the FPGA), XMD can be started.
If connecting to the UART, the window that xmd is run in serves as the UART output display.

## Slide 17: Running XMD
XMD is launched:
  Using the xmd command from the EDK Xygwin Shell
  From the XPS main Window
Notes: To launch XMD, we can use the command line in a Xygwin Shell: xmd
We can also launch it from the XPS:
- Press the button as indicated in the slide above, or
- From the main Tool Bar menu: Run  Run XMD

## Slide 18: Running XMD
We can now select the Target and connect to it using:
  mbconnect stub: for the hardware stub
Notes: To connect to the xmdstub running on the MicroBlaze™ soft processor, the Options are:
- When using an OPB JTAG UART:
mbconnect stub -comm jtag -posit 2 -chain device1.bsd … devicen.bsd
- When using the OPB UART:
mbconnect stub -comm serial -port COM2

## Slide 19: Running GDB
After loading the program, select the Target Settings...
  Enter the above settings
  Select RunConnect to target to attempt a connection from GDB to XMD
Desired debug target
Name of host running XMD
TCP port number
Notes: For GDB to be able to send and receive data from XMD, it must first be setup properly. After xmdstub is running on the target hardware and XMD is connected to the xmdstub, the debugger is ready to be run.
Run mb-gdb and set the options seen in this screen shot. Note that the TCP port number will be provided by XMD after it has been started. The Target should be TCP if XMD is running on a separate machine (such as a lab machine). If the machines are the same, then use the settings above.

## Slide 20: Outline
Introduction
Using the Debugger
Intrusive Debugging
Instruction Set Simulation
Summary

## Slide 21: Debugging Using the Instruction Set Simulator
A cycle accurate Instruction Set Simulator (ISS) is provided with the Embedded Development Kit
  No external hardware or stub is required
Code must be compiled with debug information
  mb-gcc “-g” option
  This inserts debugging information into the compiled code

## Slide 22: Running XMD
After launching XMD, we can now select the Target and connect to it using:
  mbconnect sim: for the Simulator
Notes: After launching XMD and selecting the Simulator as Target, XMD is waiting for a connection from mb-gdb.
We can use the xmd Tcl prompt simultaneously for executing xmd commands.
We will need to start mb-gdb, make a remote connection from mb gdb to xmd, download a program onto the target, and debug the program. With xmd and mb-gdb, the debugging user interface is uniform with simulation or hardware targets.

## Slide 23: Running GDB
Target...
  Select “Remote/TCP” for Cycle Accurate Simulation
    XMD needs to be running
  Select “Simulator” for functional simulation
    XMD does not need to be running
Desired Debug Target
Notes: This connects GDB to XMD and other targets. With XMD running and connected to the ISS, start GDB and set the target to TCP (this will connect GDB to XMD: this setup is the same with intrusive software debugging).
If Simulator (ISS) target is chosen (for functional simulation), then a functionally correct ISS is used and XMD does not need to be running. For Cycle Accurate Simulation, XMD must be running and the target set to Remote/TCP. After setup is complete, GDB has the same functionality as it did for Software Intrusive Debugging.
The ISS uses a model of the instruction set to simulate the processor behavior. The Cycle Accurate ISS is not only a functionally correct model of the processor, it executes each instruction in a single execution step. It uses detailed information about the pipeline behavior of the processor to provide cycle count information of the instructions being executed. Any given instruction may take several clock cycles. The functional simulation does not provide any cycle count information.

## Slide 24: Simulation Statistics
While mb-gdb is connected to XMD with the simulator target, the statistics of the cycle accurate simulator can be viewed from mb-gdb as follows:
  In the mb-gdb GUI menu, select ViewConsole
  In the console window, type monitor info
  To reset the simulation statistics, type monitor reset

## Slide 25: Outline
Introduction
Using the Debugger
Intrusive Debugging
Instruction Set Simulation
Summary

## Slide 26: Review Questions
Why is a UART needed to perform a software intrusive debugging?
What is the difference between Simple ISS and Cycle Accurate ISS?
What is required to employ software intrusive debugging?

## Slide 27: Answers
Why is a UART needed to perform a software intrusive debugging?
  You will need to place a UART on your OPB so XMD -stub can communicate with XMD. Recall XMD will be running on a local machine and transferring debug information between GDB and XMD -stub
What is the difference between Simple ISS and Cycle Accurate ISS?
  Simple ISS is a method of functionally simulating the microprocessor, while Cycle Accurate Simulation uses detailed information of the processor’s pipeline behavior to model the instruction execution and provide cycle count information. Simple ISS does not require interfacing to hardware, while Cycle Accurate Simulation does

## Slide 28: Answers
What is required to employ software intrusive debugging?
  MSS file must contain the XMDSTUB attribute
  Design must be compiled with the xmdstub option
    mb -gcc -g -xl -mode -xmdstub program.c
  XMD must be started before connection to GDB can be made
    xmd -t -hw -u gdb
  After GDB is started, use the command: FileTarget settings
    Target: Remote/TCP
    Hostname: localhost
    Port: 1234

## Slide 29: Summary
MicroBlaze offers several debugging options that are useful in all design flows, including…
  Software intrusive (with xmdstub)
Instruction Set Simulation (included with EDK)
GDB (the GNU Debugger) is a GUI interface that allows you to find your design problems
  All of these debugging methodologies require the use of GDB
XMD enables communication between the hardware and GDB
  XMD is required for all debugging methodologies described except for Simple ISS