## Slide 1: MicroBlaze Hardware Simulation

## Slide 2: Objectives
After completing this module, you will be able to:
Explain the differences between hardware and software simulation
Describe the MVS file format
Describe the function of Simgen
Specify the Simgen simulation flow

## Slide 3: Outline
Hardware vs Software Simulation
Simgen / MVS Flow
ModelSim Microprocessor Simulation
Summary

## Slide 4: Hardware vs. Software Simulation
The Embedded Development Kit (EDK) has support for both hardware and software simulation
Hardware simulation
  Output of Simgen and mb-gcc
  Used by an HDL simulator
Software simulation
  Output of mb-gcc only
  Used by gnu-debugger / xmd

## Slide 5: Hardware vs. Software Simulation
Software simulation is for testing firmware functionality
  Uses a software debugger
  Set breakpoints
  Inspect registers
  Runs on a microprocessor, or on an Instruction Set Simulator
  Quick to run
Hardware simulation is for testing peripheral and bus functionality
  Uses an HDL simulator
  You can see inspect buses
  You can test for timing violations
  Slow to run
Notes: Although technically possible, it is not feasible or recommended to use the Hardware Simulation flow to test fimware. You will have little control over the software flow, and it would not be simple to examine the stack or local variable settings. Hardware simulation is predominantly used to verify the functionality of custom peripherals before running longer tests using a software simulator.

## Slide 6: Outline
Hardware vs Software Simulation
Simgen / MVS Flow
ModelSim Microprocessor Simulation
Summary

## Slide 7: Simulation Model Flow
The Simulation Model Generator (Simgen) creates most of the files required for hardware simulation
  Inputs:
    Microprocessor verification specification (.mvs) file
    Netlists output from platgen
Outputs:
  Hardware simulation models
  Vendor-specific compilation script
Notes: The files output by simgen do not contain the processor firmware (.elf). This configuration shall be added separately.

## Slide 8: Simulation Model Flow
Simgen creates all of the VHDL to simulate peripherals and the block RAM components that hold the user object code
However, on its own, Simgen does not initialise the block RAM components with the user executable
Simgen is then run with the -i switch to initialize the memory

## Slide 9: Simulation Model Flow
Platgen
Simgen
Mb-gcc
Libgen
.vhd .do
.mhs
.mss
.mvs
.a
.elf
.bmm
Implementation
netlists
.c .cpp
Software Flow
Hardware Flow
Simulation Flow
Simgen -i
Notes: Simgen is invoked in two stages. One takes the .mhs and output of platgen, along with the .mvs file. This generates HDL output files for each peripheral and a .do file for simulator setup.
Simgen with the –I switch is invoked to add the software information to the output repository in the form of a configuration file.

## Slide 10: Sample Commands for Simulation Model Generation
Libgen -a virtexe system.mss
mb-gcc -I./include -L./lib code/system.c -o executable.elf
simgen -i executable system.mvs
Simulation models
and .do file
System_init.vhd
Platgen -a virtexe -s 2 system.mhs
simgen -a virtexe system.mvs

## Slide 11: Outline
Hardware vs Software Simulation
Simgen / MVS Flow
ModelSim Microprocessor Simulation
Summary

## Slide 12: .mvs – The Microprocessor Verification Specification
Simulation models can be in different formats:
  VHDL functional models (source)
  VHDL post-synthesis models (simprim)
  SWIFT models
Simgen uses the .mvs file to specify the simulation models to use for the microprocessor system
  We shall not be concerned with SWIFT models in this course – mainly used for Power PC designs
Notes: SWIFT models are used to describe the functionality of complex cores. This is useful to increase speed when simulating cores such as the Power PC. However, SWIFT models are not required for the MicroBlaze™ soft processor.

## Slide 13: .mvs File – Sample for MicroBlaze
PARAMETER HW_SPEC_FILE = system.mhs
PARAMETER SW_SPEC_FILE = system2.mss
PARAMETER LANGUAGE = vhdl
PARAMETER SIMULATOR = mti
BEGIN
PARAMETER HW_INSTANCE = opb_bus
PARAMETER SIM_MODEL = simprim
END
BEGIN
PARAMETER HW_INSTANCE = mylmblmb_cntlr
PARAMETER SIM_MODEL = simprim
END
BEGIN
PARAMETER HW_INSTANCE = bram1
PARAMETER SIM_MODEL = simprim
END
BEGIN
PARAMETER HW_INSTANCE = d_lmb
PARAMETER SIM_MODEL = simprim
END
BEGIN
PARAMETER HW_INSTANCE = i_lmb
PARAMETER SIM_MODEL = simprim
END
BEGIN
PARAMETER HW_INSTANCE = mytimer
PARAMETER SIM_MODEL = simprim
END
Location of the Microprocessor Hardware Specification (.mhs) file Location of the Microprocessor Software Specification (.mss) file Language to run the simulation in (VHDL or Verilog) Simulator to target (MTI or VXL)
Every configuration is within a BEGIN / END clause
Slave / Master / Bus Monitor to Configure Model to use – hdl | simprim | swift

## Slide 14: Simgen Example
Simgen is run in both modes to generate the required simulation models
  simgen -a virtexe system.mvs
  simgen -i system system.mvs
ModelSim can then be executed
  Change to the simulation directory in ModelSim, as the .do file does not use an absolute path
  Select ‘Execute Macro’ from the Macro menu
  Load the system.do file
  Setup inputs to the system (E.g., opb_clk, opb_rst, uart_rx etc.)
  Run the simulation as usual
Notes: Simgen requires platgen to have been run in order to be able to backannotate the generated netlists.
In addition, Simgen with the -i argument requires the software to have been built. This would have been generated using libgen and mb-gcc.

## Slide 15: Outline
Hardware vs Software Simulation
Simgen / MVS Flow
ModelSim Microprocessor Simulation
Summary

## Slide 16: Review Questions
What is the purpose of hardware simulation in a microprocessor system?
What is contained in the .mvs file?
What programs need to be run before
  Simgen simulation model creation?
  Simgen firmware initialization?
For a Virtex™-II device with input file system.mhs, verification specification system.mvs, and executable system.elf, which command should be used for
  Creating the simulation models?
  Configuring the block RAMs with the executable?

## Slide 17: Answers
What is the purpose of hardware simulation in a microprocessor system?
  It is used to verify the functionality of hardware components, such as custom peripherals
What is contained in the .mvs file?
  Links to the .mhs and .mss file, the HDL language to use, simulator to target, and specific peripheral simulation settings
What programs need to be run before
  Simgen simulation model creation?
  Platgen
  Simgen firmware initialization?
  Libgen and mb-gcc

## Slide 18: Answers
For a Virtex™-II device with input file system.mhs, verification specification system.mvs, and executable system.elf, which command should be used for
  Creating the simulation models?
  simgen –a virtex2 system.mvs
  Configuring the block RAMs with the executable?
  simgen –i system<.elf> system.mvs

## Slide 19: Summary
Simgen is the tool used for creating the simulation models for hardware verification
Hardware verification is good for testing peripherals and bus transactions, but not for large quantities of code
Simgen is run to create simulation models and a .do file for easy compilation into the HDL simulator.
Simgen is run with the –i switch to initialize the block RAM contents